## Slide 1: Service Assurance for Intent-based Networking Architecture & YANG Modules for Service Assurance
draft-claise-opsawg-service-assurance-architecture-02
B. Claise (Cisco), J. Quilbeuf (Cisco), Y. El Fathi (Orange), D. Lopez (Telefonica), D. Voyer (Bell Canada)
draft-claise-opsawg-service-assurance-yang-04
B. Claise (Cisco), J. Quilbeuf (Cisco), P. Lucente(NTT), P. Fasano (Telecom Italia Mobile)
IETF 107, Virtual

## Slide 2: Issues
A service being configured doesn’t mean it’s operating correctly
Too much data in telemetry: needle in a haystack
When a service degrades, where is the fault?
  what are the symptoms?
  what is the root cause?
When a network component fails, which services are impacted?
How to solve closed loop automation, as a first step

## Slide 3: Proposal
The end goal: intent-based networking
Service Assurance for Intent-based Networking Architecture proposal:
  Decompose the problem into smaller components (=subservices)
  The assurance graph links those subservices to map the service “intent”
  The subservices are assured independently
  Inferred service health score
This complement the end-to-end synthetic tests

## Slide 4: Assurance Graph
Service
Instance
Subservice
Instances

## Slide 5: Score & Symptoms
An inferred health score + a series of symptoms

## Slide 6: (Impacting or Informational) Dependencies
Impacting
Dependency
Impacting
Dependency

## Slide 7: (Impacting or Informational) Dependencies
Informational
Dependency
ECMP

## Slide 8: So far, we know…
When a service degrades, where is the fault
  what are the symptoms?
  what is the root cause?
When a network component fails, which services are impacted

## Slide 9: Open and Flexible Architecture
Open architecture for multi-vendor support
  How? With a YANG module:
    Can augment the YANG module
    Even for vendor-specific subservices
Flexible architecture:
  Components
  Service & subservices
  Distributed graph
  Physical and virtual

## Slide 10: Architecture

## Slide 11: Flexible Architecture
Could be a single box
Agent could be in or off routers

## Slide 12: Open Architecture with YANG Models
YANG
YANG

## Slide 13: Open Architecture with YANG Models
YANG
YANG
Out of scope
Out of scope

## Slide 14
module: ietf-service-assurance
+--ro assurance-graph-version? yang:counter32
+--ro assurance-graph-last-change? yang:date-and-time
+--rw subservices
+--rw subservice* [type id]
+--rw type identityref
+--rw id string
+--ro last-change? yang:date-and-time
+--ro label? string
+--rw under-maintenance? boolean
+--rw maintenance-contact string
+--rw (parameter)?
| +--:(service-instance-parameter)
| +--rw service-instance-parameter
| +--rw service? string
| +--rw instance-name? string
+--ro health-score? uint8
+--rw symptoms
| +--ro symptom* [start-date-time id]
| +--ro id string
| +--ro health-score-weight? uint8
| +--ro label? string
| +--ro start-date-time yang:date-and-time
| +--ro stop-date-time? yang:date-and-time
+--rw dependencies
+--rw dependency* [type id]
+--rw type -> /subservices/subservice/type
+--rw id -> /subservices/subservice[type=current()/../type]/id
+--rw dependency-type? identityref

## Slide 15: Assurance Tree API
module: ietf-service-assurance
+--rw subservices
+--rw subservice* [type id]
+--rw type identityref
+--rw id string
…
+--rw dependencies
+--rw dependency* [type id]
+--rw type -> /subservices/subservice/type
+--rw id -> /subservices/subservice[type=current()/../type]/id
+--rw dependency-type? identityref
Dependency relationship

## Slide 16: Health Score and Symptoms API
module: ietf-service-assurance
+--ro assurance-graph-version? yang:counter32
+--ro assurance-graph-last-change? yang:date-and-time
+--rw subservices
+--rw subservice* [type id]
….
+--ro health-score? uint8
+--rw symptoms
| +--ro symptom* [start-date-time id]
| +--ro id string
| +--ro health-score-weight? uint8
| +--ro label? string
| +--ro start-date-time yang:date-and-time
| +--ro stop-date-time? yang:date-and-time
Health score and Symptoms per subservice

## Slide 17: Subservice Parameters API
module: ietf-service-assurance
+--ro assurance-graph-version? yang:counter32
+--ro assurance-graph-last-change? yang:date-and-time
+--rw subservices
+--rw subservice* [type id]
+--rw type identityref
+--rw id string
+--ro last-change? yang:date-and-time
+--ro label? string
+--rw under-maintenance? boolean
+--rw maintenance-contact string
+--rw (parameter)?
| +--:(service-instance-parameter)
| +--rw service-instance-parameter
| +--rw service? string
| +--rw instance-name? string
Subservice Parameters
NEW
Notes: Note: A way to set a subservice as “under-maintenance”, not to receive any symptoms
  Ex: device upgrade, optic replacement, routing protocol adjustment

## Slide 18: New Subservices, with different Sets of Parameters
+--rw (parameter)?
| +--:(service-instance-parameter)
| | +--rw service-instance-parameter
| | +--rw service? string
| | +--rw instance-name? string
| +--:(service-assurance-device:device-idty)
| | +--rw service-assurance-device:device-idty
| | +--rw service-assurance-device:device? string
| +--:(service-assurance-interface:device)
| | +--rw service-assurance-interface:device? string
| +--:(service-assurance-interface:interface)
| +--rw service-assurance-interface:interface? string
| +--:(example-service-assurance-device-acme:acme-device-idty)
| +--rw example-service-assurance-device-acme:acme-device-idty
| +--rw example-service-assurance-device-acme:device? string
| +--rw example-service-assurance-device-acme:acme-specific-parameter? string
New subservice type
New vendor-specific subservice type
New subservice type
Notes: New inte

## Slide 19: Changes since Last IETF
A way to set a subservice as “under-maintenance”, not to receive any symptoms
  Ex: device upgrade, optic replacement, routing protocol adjustment
New interface health subservice with two parameters:
  1. Device id
  2. Interface id

## Slide 20: Feedback
To do: aligned with draft-irtf-nmrg-ibn-concepts-definitions
Valid problem to solve industry-wide?
At the IETF?
Going in the right direction?
If yes, please consider as WG adoption (in OPSAWG)