## Slide 1: A Layer 2 VPN Network Model (L2NM)
draft-barguil-opsawg-l2sm-l2nm-01
S. Barguil O. Gonzalez de Dios , V. Lopez (Telefonica), M. Boucadair (Orange), L. Munoz, M. Julian (Vodafone), D. King (ODC), L. Jalil (Verizon), Q. Wu (Huawei), Erez Segev (ECI Telecom)
OPSAWG Meeting 7rd Apr 2020,

## Slide 2
L2SM (RFC8466) captures an L2VPN service… but from a service standpoint
For the delivery of the service, a Network-Centric view is needed to provides a representation of the Layer 2 VPN Service from a network standpoint: L2NM
  L2NM defines a YANG module to manage the provisioning of Layer 2 VPN services within a Service Provider Network
  The module is meant to be used by a Network Controller to derive the configuration information that will be sent to relevant network devices and function
Translating L2SM into a network view is not straightforward (see next slide)
Scope & Motivation

## Slide 3: Module Structure
VPN SERVICE
[PK] service-id
service-type
status
...
VPN NODE
[PK] vpn-service-id
ne-id
import-export-profiles
...
VPN-NET-ACCESS
[PK] net-access-id
Interface-mtu
connection
...
0..n
0..n

## Slide 4: Where it Applies?
L2VPN SERVICE
PE
PE
CE
CE
VPN NETWORK ACCESS
SITE NETWORK ACCESS
TRANSPORT
IP/MPLS
BGP
SR
Assumptions:
P2P, P2PM, and MP2MP services must be supported
Several underlay transport options must be supported
VPN-NODE
VPN-NODE

## Slide 5
Module structure to fit the network view and need
And many pieces to feed that network view:
  Support newer service types such as EVPN
  Supports several types of legacy access technologies, such as ATM, FR, Ethernet, and Circuit Emulation Service (CES)
  Allows to request underlay transport protocol preference (i.e., BGP, LDP, SR-TE)
  Supports Redundancy (two remotes terminations)
  Support Network specific parameters such as RDs, RTS for BGP-VPLS
  Supports administrative & operation status
L2NM module highlights

## Slide 6
How to Contribute
The model is available on Github https://github.com/oscargdd/l2nm
Several Open Issues are discussed to improve the model, e.g.,
  Service mapping with BGP Tunnel and MPLS with LDP
  Underly tunnel selection
  E-VPN support
Collaboration with TEAS to include LNM-TE service mapping
In roadmap for vendor implementation during 2Q@2020

## Slide 7: Next Steps
Authors request the working group to review the document
Fix the open issues and comments from reviews
Consider WG adoption following L3NM way of working