## Slide 1: A Layer 3 VPN Network Yang model
draft-ietf-opsawg-l3sm-l3nm-03
O. Gonzalez de Dios, V. Lopez, S. Barguil (Telefonica)
D. Voyer (Bell Canada), L. Munoz, M. Julian (Vodafone)
D. King (ODC), L. Jalil (Verizon), A. Aguado (Nokia)
Q. Wu (Huawei), M. Boucadair (Orange),
S. Litwosky (Cisco), Erez Segev (ECI Telecom)
OPSAWG 7th April 2020,

## Slide 2: Agenda
Summary of updates from -01 version
Focus on Multicast
Auto-assign of RDs
Collaboration with TEAS: service mapping
Next steps

## Slide 3: Changes Since Last Meeting (1)
New contributors: We welcome Lucia Oliva (Telefonica), Manuel Julian (Vodafone), Erez Segev (ECI Telecom). They have contributed to complete the L3 VPN multicast and provide many contributions and insights
OPSAWG Github L3NM official Repository: https://github.com/IETF-OPSAWG-WG/l3nm
  38 issues closed. Each issue discussed in calls/mails/github
  264 commits
Multicast support fully updated. Validated in the design of Telefonica IPTV Multicast based on L3VPN
Enable requesting complex vrf-import & export profiles (AND/OR operations between communities)
  Example:
  "target:12956:184" & "target:12956:17901” | "target:12956:184" & "target:12956:1001”
Port ID identification in vpn-network-access.
  Allows to differentiate between vpn-network-access id (just an ID) and port ID (which identifies the interface/sub-interface in a device or in a topology)
Identified which BGP parameters are essentially needed as part of L3NM for operational needs.
IS-IS included as CE-PE routing protocol (one operator use case identified which required IS-IS)

## Slide 4: Changes Since Last Meeting (2)
Auto-assignment of RD solved
RT assignment is now optional (previous mandatory)
Underlay MPLS control plane preferences
  Allows the network operator to indicate its preferences: LDP, RSVP-TE tunnels, Segment Routing, BGP
  Service mapping done in collaboration with TEAS WG
vpn-node: Now only ‘ne-id’ is the key (before ‘ne-id’ and ‘vpn-id’)
  For each network element, a L3 VPN can have at most one ‘vpn-node’
Relations with other YANG modules
  L3SM and L3NM relations clarified. Text added in the draft
  Pointer to L3SM reference added in the YANG to match a service created from L3SM inputs
  List of potential device modules added
YANG module cleaned

## Slide 5: Changes Since Last Meeting (3)
Review of the I-D text
Sample Uses of the L3NM
  Enterprise L3 VPN Services
  Multi-Domain Resource Management
  Management of Multicast services
L3VPN Examples: Multicast VPN Provisioning Example added
Implementations status section:
  added ECI Telecom implementation. More implementations known, publicity subjet to management approval.

## Slide 6: BGP Parameters added to L3NM
Required for operational purposes
BGP Description: String to allow easy troubleshooting. It will be passed from L3NM to the BGP configuration in the device.
Administrative and operative Status: allows to check the health of the peering sessions directly from L3NM
Local Autonomous system: allows the operator to overwrite the A.S. A private A.S. is shown to the client (customer), while the VPN has another AS
Security: allows encryption in the BGP CE-PE session.

## Slide 7: Multicast Support
Globally:
  Update multicast container under vpn-node: multicast admin-status is managed at vrf level.
  Added anycast container within provider-managed with:
    leaf local-address: identifies the IP address of the local RP. Needed for communication between Anycast RP nodes.
    leaflist rp-set-address: list of IP address from all routers that share the same RP.
  Modify singleaddress choice by group-prefix: easier to understand parameter meaning.
  Added msdp container within multicast:
    leaf enabled: allows to control the protocol administrative status.
    leaf peer: identifies the IP address of the msdp peer
    leaf local-address: IP address of the local end of the msdp peering session
  Delete customer-tree-flavor container:
    leaflist tree-flavor located directly under multicast container.
Per access:
  Added remote-source leaf: value to identify when there is no PIM adjacency with multicast source.

## Slide 8: Auto-assignment
Three possible behaviors are needed to fulfil the identified use cases:
  The network controller auto-assigns logical resources (RTs, RDs)
  The Network Operator/Service orchestrator assigns explicitly the RTs and RDs
  The Network Operator/Service orchestrator explicitly wants NO RT/RD to be assigned
Netmod was queried for guidance
Solution proposed based on netmod feedback:
  Include explicit statement in the Yang file, e.g. if the RD leaf is not created, the entity processing the yang (the network controller) must auto-assign a value
  As value, now there is a union:
    Empty value to indicate that NO value must be assigned
    Or the desired type of the leaf (e.g. rt-types:route-distinguisher)
leaf rd {
type union {
type rt-types:route-distinguisher;
type empty;
}

## Slide 9: L3NM & TEAS Service Mapping
Joint conversations with TEAS
Requirement:
  Map L3VPN modeled with L3NM with the set of LSPs used
  Available in: https://tools.ietf.org/html/draft-ietf-teas-te-service-mapping-yang-03
module: ietf-l3sm-te-service-mapping
augment /l3vpn-svc:l3vpn-svc/l3vpn-svc:vpn-services
/l3vpn-svc:vpn-service:
+--rw te-service-mapping!
+--rw te-mapping
+--rw map-type? identityref
+--rw availability-type? identityref
+--rw (te)?
+--:(vn)
| +--rw vn-ref? -> /vn:vn/vn-list/vn-id
+--:(te-topo)
| +--rw vn-topology-id? te-types:te-topology-id
| +--rw abstract-node?
| -> /nw:networks/network/node/node-id
+--:(te-tunnel)
+--rw te-tunnel-list* te:tunnel-ref
augment /l3vpn-svc:l3vpn-svc/l3vpn-svc:sites/l3vpn-svc:site
/l3vpn-svc:site-network-accesses
/l3vpn-svc:site-network-access:
+--rw (te)?
+--:(vn)
| +--rw vn-ref?
| -> /vn:ap/access-point-list/access-point-id
+--:(te)
+--rw ltp? te-types:te-tp-id

## Slide 10: Next Steps
We believe the YANG module is now stable
Request YANG doctor review
Some text tweaking may be needed. We will work on that.
Please review this version of the document