## Slide 1: Sampled Streaming
draft-gray-sampled-streaming-03
IETF 107, Virtual Meeting
April 2020
Authors:
Andrew Gray (Charter Communications)
LJ Wobker (Cisco Systems)

## Slide 2: Problem trying to solve
We need a way to perform packet captures of links in a consistent and configurable manner.
  Inline sampling devices have to be upgraded every time link speed changes, typically lag behind, and are very expensive.
  Traditional methods of doing this tend to be limited in capabilities, and require significant on-box processing and/or control plane punting.
  Data planes are getting much faster – control planes not so much.
  We have huge datacenter infrastructures we can throw lots and lots of data at.
  We need to be able to have the device filter, and have sampling rates be variable between 1:1 (every packet) and very low sampling rates.
  We must be able to capture as many headers and as much of the payload as possible.

## Slide 3: Nomenclature from the draft
Client
Receiver
Replicator
Point
Normal Traffic Flow
Sampled Packets
Control/Negotiation

## Slide 4: Must haves
Must be very light on the on-box CPU and control plane (preferably no work at all done at the on-box control plane after set up)
  Processing terabits of traffic on the data plane – control planes can’t keep up, even at very low sampling rates (1:20,000 or worse).
Must avoid ASIC recirculation or other issues that degrade performance as much as possible.
We want one method to cover multiple vendors, capturing on servers, etc.

## Slide 5: Nice to haves
Generally a device forwarding traffic knows a lot more about a given packet than just the raw packet – getting that information off-box is useful.
  Precise receive or transmit timestamp.
  Ingress and/or egress ports or tunnels, or other actions taken.
We would also like to be able to capture/sample packets that are dropped, in addition to those being forwarded.
  Is QoS dropping the right things?
  Are we seeing drops for other reasons?
  Why is traffic being dropped or punted?

## Slide 6: Why not IPFIX extensions, OAM extensions, etc.?
  We need the raw packets.
  We would like to have a chance at getting packets that are being dropped, as well as forwarded.
  We need to be able to have different capture parameters for different types of traffic, and these can change relatively quickly.
  We are interested in whatever additional information we can get out of forwarding ASICs.
  Generally too dependent on control plane or on-box CPU.

## Slide 7: Next steps
The -01 version had code written to support (Replicator was a server, Point was effectively tcpdump, Client and Receiver were simple applications). The -02 version has a fair number of updates to the negotiation based on a lot of feedback, which has not been written into code yet.
We have gotten a lot of good feedback after announcements on the mailing list, but it has generally been unicast.
Looking for suggestions for improvement, additional use cases, or other votes of support.
Some items being worked on/discussed:
  The capture filter syntax is unique to this draft, which probably isn’t ideal.
  Additional options to communicate what a forwarding ASIC is doing with a packet.

## Slide 8: Changes from -02 (Singapore)
Feedback received during meeting and afterwards – have clarified a number of items in the draft:
  What interfaces are subject/available – everything is listed as a MAY, since hardware is different. (Examples: Subinterfaces, subscriber interfaces, and LAGs)
  How this is different than PSAMP (sampled-streaming focuses on metadata extraction and a focus on keeping the data simple enough that a forwarding ASIC can do everything on its own)
  Clarifying the handling order of sampling requests if dropped traffic is requested (explicitly state that sampling MUST occur before any other filtering in this case, and AFTER other filtering if no “dropped” traffic is desired)

## Slide 9: Requests from working group
Review the -03 draft
We really could use help with finishing up the Yang model – an attempt was made to import models from PSAMP and other locations in -03, but a pretty bad hash was made of it, and there are problems here.

## Slide 10: Q&A