## Slide 1: A Framework for Automating Service and Network Management with YANG draft-ietf-opsawg-model-automation-framework-02 OPSAWG, April 2020
Qin Wu (editor)
Mohamed Boucadair (editor)
Diego R. Lopez
Chongfeng Xie
Liang Geng
Christian Jacquenet
Luis Miguel Contreras Murillo
Oscar Gonzalez de Dios
Weiqiang Cheng
Young Lee

## Slide 2: Objectives: Reminder
Sketch an architecture framework for YANG-based automation
  Articulate common functionality to be used by multiple models and help operationalizing YANG-based model
  Discuss YANG model architecture from a network provider perspective for service and network management automation
Provide a guidance on how models at different level interconnect and glue together for service delivery and fulfillment
Exemplify how YANG models put together for service delivery and service assurance

## Slide 3: Changes since Singapore
Adopted as work item before IETF 106 Singapore meeting
Update since last version:
  Add new figures to provide examples of service connectivity components and sample attributes captured in a service model
  Clarify the use of policy in the service model, device model, and in the telemetry automation
  Fix the position of service decommission in the Service and Network Lifecycle Management
  Clarify the relation between Service Verification and Service Creation/Modification.
  Discuss the use of L3NM Capability and Notification in the L3VPN Service Delivery.
  Clarify the relation between Functional Bocks and steps to be performed in the use cases.
  Add a new use case to discuss Policy used in the Event-based Telemetry
  Security section update
  Clean up the references

## Slide 4: Data Model Layer & Representation
Layered Model Technology
Service Layer：Customer-facing model, describe service requirements, e.g., L3SM
Connectivity: Scope and Guarantees
* inter-SP connectivity (1)
* Customer to SP connectivity
* SP to any destination connectivity (3)
Flow Identification
* Destination IP address (SBC, SBE, DBE)
* DSCP marking
Traffic Isolation
Routing & Forwarding
* Routing rule to exclude ASes from the inter-domain paths
Notifications (including feedback)
* Statistics on aggregate traffic to adjust capacity
* Failures
* Planned maintenance operations
* Triggered by thresholds
Network Layer：Resource facing model, describe resource management, e.g., L3NM, Service Assurance NBI model, e.g., NBI PM model, Network Resource model, e.g., Topo model, Tunnel model
Device Layer：Describe Device Configuration parameters such as BGP, Routing Policy, QoS Model

## Slide 5: Service and Network Lifecycle Management
Service Lifecycle Management Procedure
  End to end service lifecycle management
    Service Exposure
    Service Creation/Modification
    Service Optimization
    Service Decommission
  Technology specific service lifecycle management
Service Fulfillment Management Procedure
  Intended Configuration Provision
  Configuration Validation
  Performance Monitoring
  Fault Diagnosis
Multi-layer/Multi-domain Service Mapping, e.g.:
  Service mapping between L3SM and L3NM
  Service mapping between L3NM and TE Tunnel
  Service mapping between L3NM and TE Topo
Domain specific Service Decomposing
  Service Decomposing between L3NM and a set of Network element models, e.g., BGP, ACL.
Network Element Layer
Network Layer
Network Orchestrator
Service Layer
Service Orchestrator
APP
ServiceCreation
/Modification
Service Placement
Request
Service
Placement
Request
Service
Placement
Telemetry
Service Assurance
Telemetry Notification
Service Exposure
Service Creation
/Modification
Service Optimization
Service Decomission
ServiceCreation
/Modification
Service Diagnosis
Intended
Config
Config
Validation
opstate
monitoring
Fault Diagnosis

## Slide 6: Some Missing Pieces
L3SM |
Service |
Model |
+--------------------+----------------------------+
| +-----V- -------+ |
| Orchestrator |Service Mapping| |
| +-----+---------+ |
| | |
+--------------------+----------------------------+
L3NM |
Network|
Model |
+--------------------+----------------------------+
| Controller+--------V-----------+ |
| | Service Decomposing| |
| +-++------------++---+ |
| || || |
| || || |
+-------------++---------- ++--------------------+
|| ||
|| ||
||BGP,QoS ||
|| ||
+----------+|NI,Intf,IP |+-----------------+
+--+--+ +++---+ --+---+ +--+--+
| CE1 |------| PE1 | | PE2 | ---------+ CE2 |
+-----+ +-----+ +-----+ +-----+
No feedback to the network orchestrator
No feedabck to the service

## Slide 7: Some Missing Pieces
L3SM | ^
Service | | Notifications
Model | |
+--------------------+----------------------------+
| +-----V- -------+ |
| Orchestrator |Service Mapping| |
| +-----+---------+ |
| | |
+--------------------+----------------------------+
L3NM | ^
Network| | L3NM Notifications
Model | | L3NM Capabilities
+--------------------+----------------------------+
| Controller+--------V-----------+ |
| | Service Decomposing| |
| +-++------------++---+ |
| || || |
| || || |
+-------------++---------- ++--------------------+
|| ||
|| ||
||BGP,QoS ||
|| ||
+----------+|NI,Intf,IP |+-----------------+
+--+--+ +++---+ --+---+ +--+--+
| CE1 |------| PE1 | | PE2 | ---------+ CE2 |
+-----+ +-----+ +-----+ +-----+
Expose Network service-specific capabilities and notifications
Extract relevant notifications to share

## Slide 8: YANG Data Model Integration Examples
Use Case1: L3VPN Service Delivery
Service creation
Service Mapping
Service Decomposing
Use Case2: VN Service Delivery
Service creation
Service Mapping
Service Optimization: Telemetry Model
Use Case3: Event based Telemetry
Policy Model
Telemetry Notification

## Slide 9: Next Steps
Add an explicit recommendation?
  On the importance of service-specific assurance, notification, and capabilities modules for better control and service adjustment to align with the expected service target
Add another example?
Address comments raised in the meeting
Target a WGLC in June