## Slide 1
draft-reddy-opswg-mud-tls-03
April 2020
T. Reddy (McAfee)
D.Wing (Citrix)
B.Anderson (Cisco)
MUD (D)TLS profiles for IoT devices

## Slide 2: Agenda
Recap (Solution Overview)
Updates to address comments from WG
Questions & Comments

## Slide 3: Solution overview
We propose extending MUD to describe TLS interactions.
Benefits include:
  Ability to define policies for IoT devices that have diverse communication patterns
  Robust against IoT devices learning new “skills” that change their communication patterns
  Inadequate certificate validation by some IoT devices making them vulnerable to MiTM attacks

## Slide 4: Observable (D)TLS profile parameters
We profiled several IoT devices: Amazon Echo, Echo dot, Echo Show, Fire TV, Google Home Mini, Google Home and Kindle.
  Observable (D)TLS profile parameters did not change after learning new skills
  (D)TLS profiles for IoT devices based on type, manufacturer, and model are also different
We also observed TLS profile parameters of thousands of malware flows.
Malicious (D)TLS use can be blocked

## Slide 5: Updates to draft
Highlighted the growing trend of malware using TLS.
TLS 1.3 encrypts handshake but allowing inspection of several parameters:
  List of cipher suites and extensions (e.g., supported versions, named groups, signature algorithms)
  ServerHello chosen cipher and extensions
Malware use of evasion techniques, such as ClientHello randomization, can be detected.

## Slide 6: Updates to draft
Full handshake inspection requires active participation in TLS 1.3:
  Follow the behavior defined in Section 9.3 of RFC8446 to act as a compliant TLS proxy
  TLS proxy for IT managed IoT devices
  No need to inspect payload
  Bypass acting as a proxy for connections destined to specific services due to privacy compliance requirements
Malware agents cannot mimic the thousands of unique (D)TLS profiles offered by IoT devices (type and model from several manufacturers) and cannot keep up with the updates to (D)TLS profiles.

## Slide 7
Updates to draft
Updated YANG model to define the client (D)TLS profile once and re-use it. (D)TLS profile for a specific destination (e.g., Firmware server).

## Slide 8: draft-reddy-opsawg-mud-tls-03
Comments and suggestions are welcome
Collaboration to profile IoT devices
Request for WG adoption