## Slide 1: draft-ietf-pim-igmp-mld-extension
M. Sivakumar S. Venaas
Z. Zhang
Stig Venaas presenting

## Slide 2: Overview
  A generic way of extending IGMPv3/MLDv2 messages
    Defines extension type and registry
  BIER extension moved to IGMP/MLD overlay (draft-ietf-bier-mld)
  Draft was just adopted
    Hitoshi suggested using TLVs, see later slide

## Slide 3: IGMP/MLD Additional Data
  In RFC 3376 (IGMPv3)
    4.1.10. Additional Data
    If the Packet Length field in the IP header of a received Query indicates that there are additional octets of data present, beyond the fields described here, IGMPv3 implementations MUST include those octets in the computation to verify the received IGMP Checksum, but MUST otherwise ignore those additional octets. When sending a Query, an IGMPv3 implementation MUST NOT include additional octets beyond the fields described here.
  Similar language for reports, and for queries/reports in RFC 3810

## Slide 4: Extension Type
  We think it is good to have an extension type in case there may be multiple extensions for different purposes.
  Implementations that support a specific type, process the type as defined.
  Implementations that do not support an extension type, as well as current implementations, treat it as Additional Data in the RFC and do not process the type.
  Extensions should not be common. Cannot expect router and host implementations in general to be updated.

## Slide 5: Draft currently specifies a single extension type and value
A query looks like this:
0 1 2 3
0 1 2 3 4 5 6 7 8 9 0 1 2 3 4 5 6 7 8 9 0 1 2 3 4 5 6 7 8 9 0 1
+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+
| Type = 0x11 | Max Resp Code | Checksum |
+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+
| Group Address |
+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+
| Resv |S| QRV | QQIC | Number of Sources (N) |
+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+
| Source Address [1] |
+- -+
| Source Address [2] |
+- . -+
. . .
. . .
+- -+
| Source Address [N] |
+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+
|Extension Type | Extension Value |
~ ~
+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+

## Slide 6: Extension TLV proposal
As part of adoption call, Hitoshi suggested using a TLV format. Something like the below.
0 1 2 3
0 1 2 3 4 5 6 7 8 9 0 1 2 3 4 5 6 7 8 9 0 1 2 3 4 5 6 7 8 9 0 1
+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+
| Reserved | Total Extension Length |
+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+
| Extension Type 1 | Extension Length 1 |
+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+
| Extension Value 1 |
+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+
+- . -+
. . .
. . .
+- -+
+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+
| Extension Type n | Extension Length n |
+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+
| Extension Value n |
+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+

## Slide 7: Some questions
  Do we need TLVs? Allows combination of different extensions.
  Do we need total extension length?
    It allows additional data after the TLVs
      Else we do not know when to stop processing TLVs
    We can verify that the total length matches with the length of the TLVs specified
      If implementations send additional data not following this scheme, they are unlikely to have a value here that matches the total TLV length.
      Algorithm: Loop through TLVs, add up 4 (type and length overhead) + value length for each, until >= total length.
      If equal, validation passed. Else assume not TLV extension and ignore.