## Slide 1: PIM IETF107 virtual Use of link-local in MLDv2…
No draft
Toerless Eckert (tte@cs.fau.de)

## Slide 2: Problem
Encountered in IESG review of draft using multicast discovery with assigned link-local IPv6 multicast address
  Draft-ietf-anima-autonomic-control-plane
Author (me) made normative statement MUST use MLDv2 to signal membership for LL IPv6 multicast group
  AD said this is not common practice.
    Alas that might be true (vendor implementations still not all doing this in routers.. But no idea about host implementations) Anyone ?
  Author said this is what PIM WG said should be done (do use MLDv2 for LL)
  But where is proof…

## Slide 3: IMHO…
IMHO, PIM Did/does want MLD to be used for all multicast groups, including link-local
  Experience with IPv4/IGMP not stating it explicitly -> flooding of lots of link-local, especially across snooping bridges, especially with wifi segments not needing all the link-local multicast
RFC2710 (MLDv1)
  MLD messages ARE sent for multicast addresses whose scope is 2 (link-local), including Solicited-Node multicast addresses [ADDR- ARCH], except for the link-scope, all-nodes address (FF02::1).
Gone in RF3810 (MLDv2)
  Theory: MLDv2 draft was written not by adding/changing RFC2710, but by taking RFC3376 (IGMPv3) and modding it for IPv6. Fixes from RFC2710 where lost.

## Slide 4: Current BCP , next steps ?
Applications of MLD for LL can/SHOULD (IMHO) explicitly state use of MLD for their LL (like ACP draft of mine)
  Nothing in RFC3810 stating that this can NOT be done
  Absence of ANY text about which multicast groups should use MLDv2.
    Fully up to the application when to use MLDv2
Of course, this is bad.
  Applications should be the one deciding whether to use MLDv2 or not.
Can this be solved with Errata ?
  https://www.rfc-editor.org/errata/eid5977
  Long debates on “intent” of original RFC meaning in eg.: RFC8200, but if PIM-WG agrees well enough that this was the intended meaning, …
  Approve/proceed errata state (i should know process, but i don’t).
If not errata then what ?

## Slide 5: THE END