## Slide 1: Root initiated routing state in RPL
Pascal Thubert
draft-ietf-roll-dao-projection
Interim Sept 30th, 2020
ROLL Virtual Meeting

## Slide 2: Simplifying changes
Only one main Instance / One main DODAG
Only non-storing mode main instance
Only storing P-DAO in main
Storing P-Route is strict hop by hop
And cannot be encapsulated in another track
Multiple Targets Option but just one (SR)VIO

## Slide 3: Changes Highlights (some major!)
Compressing P-DAO natively
  Using RFC 8138
Specified TrackID as a RPL instanceID
  Enables to signal the flow in the packet
  => (destination IP + local Instance)
  Missing segment ID
Added Sibling information
  Optional metrics container
  Sibling Selection out of Scope (need OF-type plug-in)
draft-ietf-roll-dao-projection
3
Interim Sept 30, 2020

## Slide 4: Changes Highlights (Cont.)
New Message to query a P-DAO
  P-DAO request and PDR-ACK
Stitching P-DAO segments
  Correlated by TrackID
  Missing stitching operation (e.g. Replication)
Aligned Track def. with 6TiSCH and RAW
Need improvements on security section
draft-ietf-roll-dao-projection
4
Interim Sept 30, 2020

## Slide 5: P-DAO Format for a Track
draft-ietf-roll-dao-projection
5
Interim Sept 30, 2020
0 1 2 3
0 1 2 3 4 5 6 7 8 9 0 1 2 3 4 5 6 7 8 9 0 1 2 3 4 5 6 7 8 9 0 1 +-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+ | TrackID |K|D| Flags | Reserved | DAOSequence | +-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+ | | + + | | + IPv6 Address of the Track Egress + | | + + | | +-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+ | Option(s)...
+-+-+-+-+-+-+-+-+

## Slide 6: Updated Route Projection Options
draft-ietf-roll-dao-projection
6
Interim Sept 30, 2020
0 1 2 3
0 1 2 3 4 5 6 7 8 9 0 1 2 3 4 5 6 7 8 9 0 1 2 3 4 5 6 7 8 9 0 1 +-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+ | Type | Option Length | Flags | SegmentID | +-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+ |Segm. Sequence | Seg. Lifetime | SRH-6LoRH header | +-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+ . . . Via Address 1 . . . +-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+ | | . .... . | | +-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+ . . . Via Address n . . .
+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+

## Slide 7: Signaling the Track in Packet
A Track is a Local Instance of the destination
Signaled in the packet in the classical RPL fashion
SRC
DEST
IPv6 Header
G/L=Local
S/D=DEST
RPLInstanceID in RPI in HbH Header
Instance
…
draft-ietf-roll-dao-projection
7
Interim Sept 30, 2020

## Slide 8: New Sibling Information option
0 1 2 3
0 1 2 3 4 5 6 7 8 9 0 1 2 3 4 5 6 7 8 9 0 1 2 3 4 5 6 7 8 9 0 1
+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+
| Type | Option Length |Comp.|B| Flags | Opaque |
+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+
| Step of Rank | Reserved |
+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+
| |
+ +
. .
. Sibling Address .
. .
+ +
| |
+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+
draft-ietf-roll-dao-projection
8
Interim Sept 30, 2020

## Slide 9: New P-DAO Request
0 1 2 3
0 1 2 3 4 5 6 7 8 9 0 1 2 3 4 5 6 7 8 9 0 1 2 3 4 5 6 7 8 9 0 1
+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+
| TrackID |K|R| Flags | PDRLifetime | PDRSequence |
+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+
| Option(s)...
+-+-+-+-+-+-+-+-+
Figure 1: New P-DAO Request Format
draft-ietf-roll-dao-projection
9
Interim Sept 30, 2020

## Slide 10: New PDR-ACK
0 1 2 3
0 1 2 3 4 5 6 7 8 9 0 1 2 3 4 5 6 7 8 9 0 1 2 3 4 5 6 7 8 9 0 1
+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+
| TrackID | PDR-ACK Status| Flags | Track Lifetime|
+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+
| PDRSequence | Reserved |
+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+
| Option(s)...
+-+-+-+-+-+-+-+
draft-ietf-roll-dao-projection
10
Interim Sept 30, 2020

## Slide 11: Pending Issues / Missing features
Signal Egress as last element in (SR)VIO?
  Useful if RFC 8138 compression
  Needed in Global instance
  Duplicate with DODAGID in Track
Inter DODAGs?
  Sibling in another DODAG?
draft-ietf-roll-dao-projection
11
Interim Sept 30, 2020

## Slide 12: Pending Issues / Missing features
Security Considerations (Ticket #179)
How P-DAO messages could be abused by
  a) rogue nodes
  b) via replay of messages
  c) if P-DAO messages may deal with any threats?
Lifetime, MOP, Retransmissions, Cleanup (Ticket #180)
Configuration parameters for Local Instance in P-DAO
  Also P-DAO parameter option in PDAO request
draft-ietf-roll-dao-projection
12
Interim Sept 30, 2020

## Slide 13: Next Steps
Gather feedback on the proposals
Remaining bugs
  Dodagid of the main dodag elided (we do only storing mode)
  Duplicate and inconsistent text
WGLC around next IETF ?
draft-ietf-roll-dao-projection
13
IETF 106 - ROLL