## Slide 1: STIR WG Interim Meeting
Assertion Values for a Resource Priority Header Claim in Support of Emergency Services Networks
(draft-dolly-stir-rph-emergency-services-00)
Monday, Apr 20 2020
Martin Dolly, and Chris Wendt

## Slide 2: Background
Personal Assertion Token (PASSporT) Extension for Resource Priority Authorization [RFC8443] extended the Personal Assertion Token(PASSporT) specification defined in [RFC8225] to allow the inclusion of cryptographically signed assertions of authorization for the values populated in the ’Resource- Priority’ header field, which is used for communications resource prioritization.
  The focus was on support of Government Priority Services RPH ‘namespaces’.
This document adds new assertion values for a Resource Priority Header ("rph") claim defined in [RFC8443], in support of Emergency Services Networks for emergency call origination and callback.
This specification defines new assertions values for:
  "ESorig": Emergency Services call origination
  "EScallback": Emergency Services callback.

## Slide 3
Proposed new Assertions
The following is an example of an "rph" claim for SIP ’Resource-Priority’ header field with a "ESorig" assertion:
    {
    "orig":{"tn":"CgPN"},
    "dest":{["tn":"911 or URN-SOS"]},
    "iat":1443208345,
    "rph":{"ESorig":["esnet,x"]}
    }
The following is an example of an "rph" claim for SIP ’Resource-
Priority’ header field with a "ESorig" assertion:
    {
    "orig":{"tn":"EmergNet Num"},
    "dest":{["tn":"CgPN that originated emergency call"]},
    "iat":1443208345,
    "rph":{"EScallback":["esnet,x"]}
    }

## Slide 4: Updates and Next Steps
Editorial cleanup
Reference for “SOS” addressing
Reference for “anonymous”
“Unregistered UE”
Need more eyes to review