## Slide 1: Service Provider OOB
IETF 107(ish)
STIR WG
Jon - @home – Apr 2020

## Slide 2: draft-peterson-stir-servprovider-oob
A new draft about using OOB in a more constrained environment
  What could you do differently if you assume the CPS is not a third-party service?
    Instead something operated by (or for) the originating or terminating domain?
  I.e., what if the entity operating the CPS would already see call signaling?
    And hence learn the called/calling party numbers
Descriptive of emerging efforts in the deployment of STIR
  Not a science project, aiming for PS

## Slide 3: Solution Components
Currently focused on the CPS being operated by the terminating service provider
  Use OOB REST interface to store PASSporTs at destination
Thus, no need to encrypt PASSporTs
  They go directly from the originating to terminating provider
    Gateways? Maybe, but only if they have a trust relationship with the originating or terminating provider
“CPS Advertisement”
  Some means of making available the CPS discoverable to calling service providers
    Propose a JSON object signed with a STIR cert

## Slide 4: Service Provider OOB
Originating SP
CPS
Store
PASSporT
Terminating
SP
Recieve
PASSporT
PSTN
POTS Call
CPS is part of the terminating administrative domain, maybe composed with VS
Call Placement Service

## Slide 5: Terminating Side CPS
May be composed with the OOB-VS
  Or may be a push interface to the VS
  Still allows CPS to be run by a third party on behalf of the terminating SP
    Multiple CPS instances may be housed in the same deployment, each pointing to a particular terminating SP
Verification process otherwise follows OOB
  Correlate PASSporT with call signaling
No need to worry over attackers querying the CPS to learn call state data
  CPS is effectively a one-way street

## Slide 6: Next Steps
Review
  Do we need this draft?
  There is a parallel effort at ATIS, aiming in particular at the SHAKEN IPNNI space
    I think the considerations here are more generic
Adoption?

## Slide 7: BACK UP