## Slide 1: SUIT Hackathon Berlin 2020

## Slide 2: Draft Progress – TEEP
TEEP Component ID structure:
  [ <TEE ID>, <Authority>, <Security Domain>, <TA name> ]
  Lazy SD instantiation
Need TAM URIs
Need TA example in SUIT draft

## Slide 3: Draft Progress – SUIT/RATS integration
Several EAT claims defined for SUIT
  Signer ID
    Component ID
      Digest
      Vendor ID (optional)
      Class ID (optional)
  Root Manifest URI
    Absolute URI
    Template (hex digest appended to template)
  Root Manifest Digest

## Slide 4: Draft Progress – Authentication Wrapper encoding
The Authentication Wrapper contains COSE objects
  Wrapping these objects in bstr would probably make them more consumable by COSE libraries

## Slide 5: Draft Progress – Digest in COSE payload
The COSE payload for SUIT is now a SUIT_Digest of the manifest
  This may help if using EdDSA, since RFC8152 does not support HashEdDSA
  This helps for modular processing of large PQC signatures

## Slide 6: Draft Progress – Reference URI
It may be helpful to provide a reference URI that can be used to obtain a complete copy of a manifest
This may be a template so that a hex digest, appended to the URI will resolve to a URI for the complete manifest

## Slide 7: Draft Progress – Vendor/Class ID examples
The examples do not match the CDDL.
  The Vendor ID & Class ID are parameters in CDDL
  The examples show vendor ID and class ID conditions taking UUID arguments

## Slide 8: Draft Progress – Try Each Examples
The examples for Try Each do not have bstr wrappers on each sequence, but the CDDL does

## Slide 9: Draft Progress – Minimal Loops
A loop over each component appears to be a good optimization.
  This satisfies loading a flash component ID into a RAM component ID and having them share a digest.
Map-Test-Execute has not yet been demonstrated. Not sure if it is needed.
  There have been requests for prioritized parameter lists, so this may still be needed.