## Slide 1: IETF Definition of Transport Slice
draft-nsdt-teas-transport-slice-definition-02
(R. Rokui, Nokia; S. Homma, NTT, L. Contreras, Telefonica, K. Makhijani, Futurewei)
+ the entire NSDT

## Slide 2: Scope
Definition of the Transport Slice
Characteristics and Terminology
Structure of a Transport Slice
Role of Transport slice in E2E Slices

## Slide 3: Definition
"A transport slice is a logical network topology connecting a number of endpoints and a set of shared or dedicated network resources, which are used to satisfy specific Service Level Objectives (SLO)".
  Logical Description => technology agnostic or independent
    Its Realization will be specific to underlying technology.
  Service level objectives => concrete resource (and connection) requirements
  Topology & end points => connectivity centric, other related things are handled at a level above.

## Slide 4: Characteristics: 1. Service Level Objectives
What kind of SLOs ( concrete - reuse definitions from existing work)
  Guaranteed Bandwidth: assurance of minimum or range of the bandwidth requirement.
  Guaranteed Latency [RFC 2681/7679]: maximum permissible, excluding application processing delay.
  Packet delay variation (PDV)/Jitter [RFC3393]
  Packet loss rate [7680]
  NF resources – [Ref: ETSI NFVI] Compute, Interface, Memory + function specific.
Characteristics (a) Service Level Objectives (b) Endpoint types (c) Vertical Transport Slice (d) Horizontal Composition

## Slide 5: Characteristics: 1. Service Level Objectives Contd.
What kind of SLOs (operational)
  Availability: concerns with how quickly network becomes available after a fault. Use Meant time between failures (MTBF), and Mean time to repair (MTTR).
  Reliability and resource redundancy attributes - a backup or duplicate resources such as path (same SLOs - latency, bandwidth, etc.), network functions (same compute, memory, etc.)
  Security: The objective of securing a transport slice concern with three attributes:
    End-to-end encryption between endpoints: logical link requiring encryption,
    Authentication and access control (ACLs) objectives
    Isolation characteristic to prevent interference between two or more slices or other flows on the same infrastructure.
Characteristics (a) Service Level Objectives (b) Endpoint types (c) Vertical Transport Slice (d) Horizontal Composition

## Slide 6: Characteristics: Service Level Objectives –Contd. Isolation, SLO violations
Resolution of Guarantee:
  Defined in terms of resource interference (consequence of sharing)
  Soft guarantees of resources: describe tolerance to interference
  Hard guarantees: Not affected by other traffic. How to implement this – upto the provider. For example: may have dedicated resource reservation
Isolation and SLO violations
  Should be a derivable attribute. From availability characteristics (failures period, repair times)
  Isolation itself doesn’t imply that violations cannot occur.
    Due to resource contention
    Due to faults (covered by protection, restoration, redundancy)
Characteristics (a) Service Level Objectives (b) Endpoint types (c) Vertical Transport Slice (d) Horizontal Composition

## Slide 7: Characteristics: End points
What kind of Endpoints
  Transport type: Nodes performing forwarding functions (routers, switches, gateways)
  Service Type: Nodes performing network-service functions e.g. DPI, firewall, NAT.
(Multi-)point to (multi-)point connectivity patterns
  Creates dependency on scale and specification of SLOs. Between 2 endpoints or from multiple endpoints to an endpoint.
Characteristics (a) Service Level Objectives (b) Endpoint types (c) Vertical Transport Slice (d) Horizontal Composition

## Slide 8: Characteristics: Horizontal and Vertical Slices
Horizontal Slices
  connect 2 TSes at the same level.
  Use case: TS11: L2VPN segment + TS12: SRV6.
Vertical Slices
  Hierarchical representation, stitching at a layer above (ƛ-> IP)
  Use case: TS121 and TS122: are 2 optical networks and are combined into a single slice TS12
Mechanisms at provider level:
  Slice Stitching gateways (work in progress)
Characteristics (a) Service Level Objectives (b) Endpoint types (c) Vertical Transport Slice (d) Horizontal Composition
How to Extend transport slices to meet different service requirements

## Slide 9: Structure of Transport Slices
Stakeholders – for terminology consistency - define actors, roles
Defines NBI and SBI – details in Framework draft.
Dual aspect of transport slice -
  A description that is purely technology agnostic
  Its Realization – this may require one or more technology specific ‘materializing’ in provider networks.
Realization
A transport slice for a service vertical
Structure: (a) Stakeholders (b) TSC Interfaces (c)Transport slice Realization

## Slide 10: Role of Transport slice in E2E Slices
City CCTV use case: Combination of transport slices and other slices such as RAN etc.
<======================= E2E NS ======================>
<-OS1-> <-TS1-> <-TS2-> <-OS2-> ... <-TSn-> <-OSm->
|------------------------------------------------------|
| .--. .--. .--. |
| ( )--. ( )--. ( )--. |
| .' ' .' ' .' ' |
[EU-x] | ( Network-1 ) ( Network-2 ) ... ( Network-p ) |[EU-y]
| `-----------' `-----------' `----------' |
| |
| Operator-z |
|------------------------------------------------------|
Legend:
E2E NS: End-to-end network slice
TSn: Transport Slice n
OSm: Other Slice m
EU-x: End User-x
EU-y: End User-y
Figure 4: E2E network slice

## Slide 11: Summary + Next Steps
Summary
  Definitions document establishes baseline of concepts and terminology and scope to some extent.
  Intentionally kept concise and is independent of any pre-determined technology.
  Fully aligned with terms and description in framework draft.
Next Steps
  Feedback
  Ready for WG adoption?