## Slide 1: Applicability of ACTN to Packet Optical Integration (POI)
draft-peru-teas-actn-poi-applicability-03
Fabio Peruzzini - fabio.peruzzini@telecomitalia.it
Italo Busi - Italo.busi@huawei.com
Jean-Francois Bouquier - jeff.bouquier@vodafone.com
Michael Scharf - michael.Scharf@hs-esslingen.de
Sergio Belotti - sergio.belotti@nokia.com
Young Lee - younglee.tx@gmail.com
Daniele Ceccarelli - daniele.ceccarelli@ericsson.com
Jeff Tantsura - jefftant.ietf@gmail.com
Daniel King - daniel@olddog.co.uk

## Slide 2: The Motivation for this Work
Definition of key use cases for Packet Optical Integration (POI), described both from the point of view of the optical and packet layer
Document the process and required coordination interactions between
IP and Optical network components
Identification of the IETF protocols and data models that may be used for ACTN-based infrastructure to control of POI networks, specially:
  the MDSC (Multi-Domain Service Coordinator) and
  underlying Packet and Optical Domain Controllers (P-PNC and O-PNC)
This will help us understand the current level of standardization and, highlight gaps, if any:
Are the existing models suitable?
  If not, what is missing?
Any operational issues that need addressing?
  Operational
  Security

## Slide 3: Use Cases Described
Multi-Layer Topology Coordination | 
1.1 | Discovery of existing Och, ODU, IP links, IP tunnels and IP services
1.2 | Provisioning of an IP Link/LAG over the DWDM
1.3 | Provisioning of an IP link/LAG over DWDM with path constraints
1.4 | Provisioning of an additional link member to an existing LAG with or without path constraint
Multi-Layer Recovery Coordination | 
2.1 | Ensuring network resiliency during maintenance events
2.2 | Router port failure
Service Coordination Across a Multi-Layer Network | 
3.1 | Based on an L2 / L3 / VN Service Request

## Slide 4: Current Reference Topology
Optical Domain PNC
MDSC
Packet Domain
PNC
Packet Domain PNC
Optical Domain PNC
Optical Transport
Optical Transport`
IP
Domain
IP
Domain
MPI
MPI MPI
MPI

## Slide 5: Current state of the Document
Merge of draft-lee-teas-actn-poi-applicability-00 into draft-peru-teas-actn-poi-applicability-03
Current document now includes…
  Discusses methods for:
    discovering existing links and IP tunnels
    populating topology
    inter-domain link discovery
  Documents the YANG models used for the use cases
    common YANG models used
    models used at the Optical MPIs
    models at the Packets MPIs
    model for TE Service Mapping
  Documents procedure for Service Coordination for Multi-layer Networks
    how the L2SM, L3SM and VN, YANG models would be used

## Slide 6: Next steps for the Document
Additional clean up of text merged from draft-lee-teas-actn-poi-applicability-00
Documenting options to discover inter-domain links at MDSC level
Review the applicability of IP and WDM inventory models
Need to discuss Operational Considerations in more detail
  Such as the applicability of management and telemetry methods and relevant models
Further discussion of Security Considerations
  A need to consider malicious attack and rogue elements attempting to connect to various ACTN components, and how to negate or mitigate
Issue tracking and current version available on Git
  Currently we are tracking 12 open issues
  https://github.com/FabioPeruzzini/actn-poi

## Slide 7: Questions for the working group
Is this still a useful activity for the working group?
  Describing key ACTN POI use cases and how to solve them
    Including the requirements, and the models that may be applied to service them, highlighting model gaps, and operational and security considerations
If so, is it time for the TEAS WG to adopt the work?