## Slide 1
A Yang Data Model for Transport Slice
draft-wd-teas-transport-slice-yang-01
TEAS WG
April 23, 2020
Bo Wu (Presenting), Dhruv Dhody Huawei
Liuyan Han China Mobile
Reza Rokui Nokia

## Slide 2: Transport Slice Model - Overview
nsdt-teas-transport-slice-definition
  "A transport slice is a logical network topology connecting a number of endpoints and a set of shared or dedicated network resources, which are used to satisfy specific Service Level Objectives (SLO)".
nsdt-teas-ns-framework
  “The NBI uses protocol mechanisms and information passed over passed over those mechanisms to convey desired attributes for transport slices and their status. The information is expected to be represented as a well-defined data model, and should include at least endpoint and connectivity information, SLO specification, and status. ”
Transport Slice NBI YANG model definition
  Abstract topology: Endpoint and connectivity information
  SLO policy: Includes bandwidth, latency, Jitter, packet loss etc.
  Status information: Includes performance statistics and also operational status
Network Controller(s)
Transport Slice Controller
Customer
A higher level system
TSC NBI
TSC SBI

## Slide 3: Yang Modeling Options for TS-NBI
Augmenting VN model (ACTN)
Augmenting IETF network model (RFC 8345)
Independent model
Create a transport-slice yang model by augmenting the ietf-vn model
Create a transport-slice yang model by augmenting the ietf-network & ietf-network-topology model
Create an independent model
Author’s preference for this I-D!
Better suited for Transport Slice Realization
as TS-SBI, that maps transport slice (customer view) to provider network!

## Slide 4: Transport Slice Modeling
Transport slice modeling basic constructs
Customer view of a transport slice
transport slice model
transport slice list
ts-end point
ts-member
ts-slo-group
TS-SLO-Group Red TS-SLO-Group Blue
TS-Member 2 EP1-EP3 TS-Member 1 EP1-EP2
TS-Member 3 EP1-EP4
TS-Member 4 EP2-EP3
TS-Member 5 EP2-EP4
TS-Endpoint: is a logical identifier to identify the access point of a Transport Slice, that can be further mapped. It also includes traffic-matching criteria
TS-Member: is a logical connection between any two TS endpoints, point-to-point and unidirectional
TS-SLO-Group: is a group of TS-members with the same SLOs in one Transport Slice

## Slide 5
module: ietf-transport-slice
+--rw transport-slices
+--rw slice-templates
| +--rw slice-template* [id]
| +--rw id string
| +--rw template-description? string
+--rw transport-slice* [ts-id]
+--rw ts-id uint32
+--rw ts-name? string
+--rw ts-topology* identityref
+--rw ts-slo-group* [slo-group-name]
| +--rw slo-group-name string
| +--rw default-slo-group? boolean
| +--rw slo-tag? string
| +--rw (slo-template)?
| | +--:(standard)
| | | +--rw template? leafref
| | +--:(custom)
| | +--rw ts-slo-policy
| | +--rw isolation-type? identityref
| | +--rw bandwidth? te-types:te-bandwidth
| | +--rw latency
| | | +--rw one-way-latency? uint32
| | | +--rw two-way-latency? uint32
| | +--rw jitter
| | | +--rw one-way-jitter? uint32
| | | +--rw two-way-jitter? uint32
| | +--rw loss
| | | +--rw one-way-loss? decimal64
| | | +--rw two-way-loss? decimal64
| | +--rw ts-metric-bounds
| | | +--rw ts-metric-bound* [metric-type]
| | | +--rw metric-type identityref
| | | +--rw upper-bound? uint64
| | +--rw availability-type? identityref
| +--rw ts-member-group* [ts-member-id]
| | +--rw ts-member-id leafref
| +--ro slo-group-monitoring
| +--ro latency? uint32
| +--ro jitter? uint32
| +--ro loss? decimal64
+--rw status
| +--rw admin-enabled? boolean
| +--ro oper-status? operational-type
+--rw ts-endpoint* [ep-id]
| +--rw ep-id uint32
| +--rw ep-name? string
| +--rw ep-role* identityref
| +--rw geolocation
| | +--rw altitude? int64
| | +--rw latitude? decimal64
| | +--rw longitude? decimal64
| +--rw node-id? string
| +--rw tp-id? string
| +--rw ts-traffic-criteria
| | +--rw ts-traffic-criteria* [match-type]
| | +--rw match-type identityref
| | +--rw value? string
| +--rw site-access-parameters
| | +--rw site-name? string
| | +--rw availability-priority? uint32
| +--rw bandwidth-slo
| | +--rw incoming-bandwidth
| | | +--rw guaranteed-bandwidth? te-types:te-bandwidth
| | | +--rw max-bandwidth? te-types:te-bandwidth
| | +--rw outgoing-bandwidth
| | +--rw guaranteed-bandwidth? te-types:te-bandwidth
| | +--rw max-bandwidth? te-types:te-bandwidth
| +--rw mtu uint16
| +--rw protocol
| | +--rw vrrp
| | | +--rw float-ipv4? inet:ipv4-prefix
| | | +--rw float-ipv6? inet:ipv6-prefix
| | +--rw bgp
| | | +--rw bgp-peer-ipv4* inet:ipv4-prefix
| | | +--rw bgp-peer-ipv6* inet:ipv6-prefix
| | +--rw static
| | +--rw static-route-ipv4* inet:ipv4-prefix
| | +--rw static-route-ipv6* inet:ipv6-prefix
| +--rw status
| | +--rw admin-enabled? boolean
| | +--ro oper-status? operational-type
| +--ro ep-monitoring
| +--ro incoming-utilized-bandwidth? te-types:te-bandwidth
| +--ro incoming-bw-utilization decimal64
| +--ro outgoing-utilized-bandwidth? te-types:te-bandwidth
| +--ro outgoing-bw-utilization decimal64
+--rw ts-member* [ts-member-id]
+--rw ts-member-id uint32
+--rw src
| +--rw src-ts-ep-id? leafref
+--rw dest
| +--rw dest-ts-ep-id? leafref
+--rw monitoring-type? ts-monitoring-type
+--ro ts-member-monitoring
+--ro latency? uint32
+--ro jitter? uint32
+--ro loss? decimal64
SLO policy
Monitoring

## Slide 6: Transport Slice Topology and TS Endpoint
TS-EP is a logical identifier to identify the logical access point of a Transport Slice, and there are three options for different scenarios
Per slice “ts-topology” and “ep-role” of TS-EP
Transport
Scenario#1:
EP is an interface
on Customer Site
Scenario#2:
EP is an interface
on PE
Scenario#3:
EP is a logical
Interface at either
or both
Customer
Site
PE
Transport
Transport
Port 2/2
170.1.1.1/29
EP
EP
EP
EP
Port 1/1

## Slide 7: Transport slice SLO (1)
Transport Slice SLO policy definition: we plan to reuse the TE-Types grouping definition as much as possible
  This is work in progress!
The simplest scenario is that the connections between any two endpoints in a slice meet the same SLO policy
  all TS-members are part of a single TS-Slo-group!
Per TS, ts-slo-group
+--rw ts-slo-policy
+--rw isolation-type? identityref
+--rw bandwidth? te-types:te-bandwidth
+--rw latency
| +--rw one-way-latency? uint32
| +--rw two-way-latency? uint32
+--rw jitter
| +--rw one-way-jitter? uint32
| +--rw two-way-jitter? uint32
+--rw loss
| +--rw one-way-loss? decimal64
| +--rw two-way-loss? decimal64
+--rw ts-metric-bounds
| +--rw ts-metric-bound* [metric-type]
| +--rw metric-type identityref
| +--rw upper-bound? uint64
+--rw availability-type? identityref
Per TS-Endpoint
+--rw bandwidth-slo
| +--rw incoming-bandwidth
| | +--rw guaranteed-bandwidth? te-types:te-bandwidth
| | +--rw max-bandwidth? te-types:te-bandwidth
| +--rw outgoing-bandwidth
| +--rw guaranteed-bandwidth? te-types:te-bandwidth
| +--rw max-bandwidth? te-types:te-bandwidth

## Slide 8: Transport slice SLO (2)
TS-Member: is a logical connection between any two TS endpoints, point-to-point and unidirectional.
Different SLOs for different parts of the same slice
  “ts-slo-group” define a set of ts-member that meet the same TS SLO
  Some scenarios in NS DT discussion:
    Different bandwidth guarantee of “connection of gNBs to UPF with co-located content server ”
    Different Latency in each constituent part “some connections of gNBs to UPF with co-located content server, and some connections of gNBs to UPF with VR/AR system ”
    Network sharing: on-fly change requests to some connections to a new SLO
CN
AN1
AN2
TN1-1
TN1-2
TN1-3
TN1-4
CN1
CN2
TN1-3
TN1-4
TS-SLO-Group Red TS-SLO-Group Blue
TS-Member 2 EP1-EP3 TS-Member 1 EP1-EP2
TS-Member 3 EP1-EP4
TS-Member 4 EP2-EP3
TS-Member 5 EP2-EP4

## Slide 9: Transport Slice monitoring
Transport Slice monitoring in various granularity, which reports to the upper-layer management system to quickly locate the affected customer services in particular part or particular site
  Per TS SLO group: Per group of connections performance and status
  Per TS connection : Per connection periodic or on-change (TCA) performance and status
  Per TS Endpoint: Performance status of bandwidth utilization for incoming and outgoing
The mechanism defined in [RFC8640] can be used for either periodic or on-demand subscription of TS operational and performance status
Threshold Crossing Alert (TCA) still in discussion
TS-SLO-Group Red TS-SLO-Group Blue
TS-Member 2 EP1-EP3 TS-Member 1 EP1-EP2
TS-Member 3 EP1-EP4
TS-Member 4 EP2-EP3
TS-Member 5 EP2-EP4
Notes: ? uint32
| +--ro jitter? uint32
| +--ro loss? decimal64

## Slide 10: Open issues
A brand new model, or an augmented model based on existing IETF model, e.g. VN model?
Transport slice endpoint definition
“ts-slo-group”: Different SLOs for different parts of the same slice

## Slide 11: Next Step:
Solicit reviews and comments from WG
WG Adoption

## Slide 12
Backup slides

## Slide 13: TS-NBI as Augmenting VN model (ACTN)
ietf-vn
AP
VNAP
VN
VN-Member
From
To
Augmented TS-Endpoint details
Augmented TS-Slice details
Augmented TS-Member details
SLO groups
Node
connectivity-matrices
underlay
primary-path
path-constraints
Optimizations
computed-path-properties
connectivity-matrix [id]
From
underlay
Primary-path
path-constraints
Optimizations
To
tunnel-termination-points
tunnel
A tight coupling with TE topology abstract node & connectivity matrix!
After all VN and TE Yang model is just one of the many slice realization techniques!

## Slide 14: Relationship with VN/TE topo model
Transport Slice model is an independent model.
The VN model is tightly coupled with the TE topology model.
ACTN VN Yang Model
AP
VN
VN-Member
VNAP
A Virtual Network Access Point (VNAP) is the binding between an AP and a VN.
A different VNAP is created on an AP for each VN.
AP is shared between multiple VN
VN is abstract node in TE topo model
Connectivity
Matrix
Transport Slice Model
Transport slice
TS-end point
TS-Member
VN 1
VN 1
VN 2

## Slide 15: TS-NBI as Augmenting network model (RFC8345)
ietf-network
Node
supporting-node*
Termination-point*
Link*
Source
Destination
Supporting-link*
networks
supporting-network*
Supporting-termination-point*
Augmented TS-Slice details
SLO groups
Augmented TS-Endpoint details
Augmented TS-Member details
ietf-network-topology
Network hierarchy are useful for provider to map slice to provider network but not as a customer view of the transport slice
Augmenting TP via TS-Endpoint loses the logical nature of this identifier and require one to maintain abstract nodes for customer site (CE) and PE even when unknown.
Other option would be to model TS-Endpoint as node