## Slide 1
Trustworthy Multipurpose Remote Identification
(tm-rid) Interim Webex 2010 FEB 06 THU:
Proposed Architecture
Progress & Next Steps to add strong authentication techniques to identify physically nearby objects
Stu Card, Adam Wiethuechter

## Slide 2: Terminologies of the 2 worlds collide
UAS (ASTM & CAAs)
UA: Unmanned Aircraft
GCS: Ground Control Station
UAS: Unmanned Aircraft System (UA + GCS)
USS: UTM Service Supplier
SDSP: Supplemental Data Service Provider
UTM: UAS Traffic Management
UVR: UAS Volume Reservation
UAS RID: UAS Remote Identification
TMRID: Trustworthy Multipurpose Remote ID
Internet (IETF & ICANN)
DNS: Domain Name System
RR: Resource Record (in DNS)
WHOIS: domain name registry lookup tool
RDAP: Registry Data Access Protocol
EPP: Extensible Provisioning Protocol
HIP: Host Identity Protocol
[H]HI[T]: [Hierarchical] Host Identity [Tag]
Certificate: HHIT + HI, w/expiration, signed w/HI(priv)
  Cxy is a certificate signed by Entity X, attesting to the veracity of a claim made by Entity Y

## Slide 3
Unmanned Aircraft System (UAS) Remote Identification (RID): Motivation for Proposed Architecture
Recap…
ASTM F38.02 WK65041 UAS RID… Broadcast RID… Network RID…
FAA (US) NPRM… Standard RID… Limited RID… error correction… cybersecurity… also EASA (EU) regs soon to take effect…
Leverage existing Internet services/infrastructure/protocols (e.g. WHOIS/RDAP, EPP, DNS, HIP).
  Strengthen authentication, balance operator privacy w/genuine Need To Know…
(UA physical location : UA ID) ~ (host logical location (IP) : host ID)
  We have prototyped & flown a HIP based extension to OpenDroneID.
  Manufacturer assigned Hardware Serial Number per ANSI/CTA-1063-A (ASTM UAS ID Type 1)
  UTM system assigned Session ID (ASTM UAS ID Type 3 UUID): “randomly-generated alphanumeric code that is used only for one flight” (p. 21, NPRM)

## Slide 4: UPP2 Use Case 4

## Slide 5: AXE UPP2 Use Case 5

## Slide 6: Goal: Make RID Received Information Immediately Actionable -> Sub-Goals
make it trustworthy (despite severe constraints of Broadcast RID)
enable verification that an UAS is registered
  if so, in which registry (for classification of trusted operators on the basis of known registry vetting, even by observers lacking Internet connectivity at observation time)
enable instant establishment, by authorized parties, of secure communications with the remote pilot

## Slide 7: tm-rid General Req’s for UAS
verify that messages originated from the claimed sender
verify that the UAS ID is in a registry & identify which one
lookup, from the UAS ID, public information
lookup, w/AAA, per policy, private information
structure information for both human and machine readability
provision registries with
  static information on the UAS & its Operator / Pilot In Command / Remote Pilot
  dynamic information on its current operation within the UTM
  Internet direct contact information for services related to the foregoing
close the AAA-policy registry loop by
  governing AAA per registered policies
  administering policies only via AAA
dynamically establish, w/AAA, per policy, E2E strongly encrypted communications w/the UAS RID sender & entities looked up from the UAS ID, inc. the GCS & USS
It is highly desirable that Broadcast RID receivers also be able to stamp messages with accurate date/time received and receiver location, then relay them to a network service (e.g. distributed ledger), inter alia for correlation to assess sender & receiver veracity.

## Slide 8: tm-rid General Req’s for UAS easily satisfied if UAS ID is a HHIT in DNS & Whois (w/RDAP, EPP & XACML)
verify that messages originated from the claimed sender
verify that the UAS ID is in a registry & identify which one
lookup, from the UAS ID, public information
lookup, w/AAA, per policy, private information
structure information for both human and machine readability
provision registries with
  static information on the UAS & its Operator / Pilot In Command / Remote Pilot
  dynamic information on its current operation within the UTM
  Internet direct contact information for services related to the foregoing
close the AAA-policy registry loop by
  governing AAA per registered policies
  administering policies only via AAA
dynamically establish, w/AAA, per policy, E2E strongly encrypted communications w/the UAS RID sender & entities looked up from the UAS ID, inc. the GCS & USS
It is highly desirable that Broadcast RID receivers also be able to stamp messages with accurate date/time received and receiver location, then relay them to a network service (e.g. distributed ledger), inter alia for correlation to assess sender & receiver veracity.

## Slide 9: tm-rid General Req’s for UAS easily satisfied if UAS ID is a HHIT w/proposed new crypto in DNS & Whois
verify that messages originated from the claimed sender
verify that the UAS ID is in a registry & identify which one
lookup, from the UAS ID, public information
lookup, w/AAA, per policy, private information
structure information for both human and machine readability
provision registries with
  static information on the UAS & its Operator / Pilot In Command / Remote Pilot
  dynamic information on its current operation within the UTM
  Internet direct contact information for services related to the foregoing
close the AAA-policy registry loop by
  governing AAA per registered policies
  administering policies only via AAA
dynamically establish, w/AAA, per policy, E2E strongly encrypted communications w/the UAS RID sender & entities looked up from the UAS ID, inc. the GCS & USS
It is highly desirable that Broadcast RID receivers also be able to stamp messages with accurate date/time received and receiver location, then relay them to a network service (e.g. distributed ledger), inter alia for correlation to assess sender & receiver veracity.

## Slide 10: tm-rid General Req’s for UAS easily satisfied if UAS ID is a HHIT w/proposed new crypto in DNS & Whois, plus HIP is deployed on participating UTM nodes
verify that messages originated from the claimed sender
verify that the UAS ID is in a registry & identify which one
lookup, from the UAS ID, public information
lookup, w/AAA, per policy, private information
structure information for both human and machine readability
provision registries with
  static information on the UAS & its Operator / Pilot In Command / Remote Pilot
  dynamic information on its current operation within the UTM
  Internet direct contact information for services related to the foregoing
close the AAA-policy registry loop by
  governing AAA per registered policies
  administering policies only via AAA
dynamically establish, w/AAA, per policy, E2E strongly encrypted communications w/the UAS RID sender & entities looked up from the UAS ID, inc. the GCS & USS
It is highly desirable that Broadcast RID receivers also be able to stamp messages with accurate date/time received and receiver location, then relay them to a network service (e.g. distributed ledger), inter alia for correlation to assess sender & receiver veracity.

## Slide 11: tm-rid Req’s for UAS Identifiers
20 bytes or smaller
sufficient to identify a registry in which the UAS is listed
sufficient to enable lookup of other data in that registry
unique within a to-be-defined scope
non-spoofable within the context of Remote ID broadcast messages (some collection of messages provides proof of UA ownership of ID).
A tm-rid UAS ID MUST NOT facilitate adversarial correlation of UAS operational patterns; this may be accomplished e.g. by limiting each identifier to a single use, but if so, the UAS ID MUST support defined scalable timely registration methods.
Mechanisms standardized in tm-rid MUST be capable of proving ownership of a claimed UAS ID, and SHOULD be capable of doing so immediately on an observer device lacking Internet connectivity at the time of observation.
Mechanisms standardized in tm-rid MUST be capable of verifying that messages claiming to have been sent from a UAS with a given UAS ID indeed came from the claimed sender.

## Slide 12: tm-rid Req’s for UAS Identifiers satisfied by a HHIT in DNS & Whois (w/RDAP, EPP & XACML)
20 bytes or smaller
sufficient to identify a registry in which the UAS is listed
sufficient to enable lookup of other data in that registry
unique within a to-be-defined scope
non-spoofable within the context of Remote ID broadcast messages (some collection of messages provides proof of UA ownership of ID)
A tm-rid UAS ID MUST NOT facilitate adversarial correlation of UAS operational patterns; this may be accomplished e.g. by limiting each identifier to a single use, but if so, the UAS ID MUST support defined scalable timely registration methods.
Mechanisms standardized in tm-rid MUST be capable of proving ownership of a claimed UAS ID, and SHOULD be capable of doing so immediately on an observer device lacking Internet connectivity at the time of observation.
Mechanisms standardized in tm-rid MUST be capable of verifying that messages claiming to have been sent from a UAS with a given UAS ID indeed came from the claimed sender.

## Slide 13: tm-rid Req’s for UAS Identifiers satisfied by a HHIT in DNS & Whois (w/RDAP, EPP & XACML) used for only 1 UAS flight
20 bytes or smaller
sufficient to identify a registry in which the UAS is listed
sufficient to enable lookup of other data in that registry
unique within a to-be-defined scope
non-spoofable within the context of Remote ID broadcast messages (some collection of messages provides proof of UA ownership of ID)
A tm-rid UAS ID MUST NOT facilitate adversarial correlation of UAS operational patterns; this may be accomplished e.g. by limiting each identifier to a single use, but if so, the UAS ID MUST support defined scalable timely registration methods.
Mechanisms standardized in tm-rid MUST be capable of proving ownership of a claimed UAS ID, and SHOULD be capable of doing so immediately on an observer device lacking Internet connectivity at the time of observation.
Mechanisms standardized in tm-rid MUST be capable of verifying that messages claiming to have been sent from a UAS with a given UAS ID indeed came from the claimed sender.

## Slide 14: Encode a HHIT as an ASTM UAS ID Type 1
Comply w/ANSI-CTA-2063-A.
Set length field to “F” encoding value 15.
In 15 character serial “number” field, encode:
  last nibble of IANA HHIT prefix (1 char);
  ORCHID Generating Algorithm ID (1 char);
  64 bit hash of HI (13 chars, 5 bits each).
In DNS, map 4 character Manufacturer ID to a HHIT registry (RRA + HDA).
Also map UAS ID Type 3 values to HHITs in DNS: big questions of scalability?

## Slide 15
tmrid: operator registration
Operator generates HI keypair (HIo / HIo(priv)) along with cert Coo.
Operator sends Coo to Registry.
Registry validates Coo and makes decision to add Operator to Registry.
Registry (using its HI keypair) will create Cro and securely sends it back to Operator for confirmation.

## Slide 16: tmrid: registration details
When registering Operator use secure web methods (HTTPS, etc.) to perform all information transfers
  HIP is an option if available between hosts (such as during UA registration with Operator acting on UA behalf)
When keypairs are generated HHITs are proposed
  RRA and HDA for Registry to be used should be already known, allowing for Operator/UA to synthesize HHIT
  Registry checks for HHIT collisions for UA to decide if accepted – if collision then Registry signals back to device to regenerate HI (same for Operator?)
    Fulfills requirement of an ASTM “UTM Assigned ID” and FAA NPRM “Session ID” (similar mechanism to IP negotiation in a networks)
Open questions
  What exactly is in each certificate?

## Slide 17
tmrid: ua registration
(1) Operator creates HI keypair for UA (HIa / HIa(priv)), generates cert Caa using them.
Operator using his keypair creates Coa.
(3) Registry validates Caa, plus inspects Coa and makes decision to add UA to Registry.
Registry (using its HI keypair) creates Croa as proof of registration of UA to Operator.
Registry also creates Cra to be used in TMRID Auth. Message.
(5) Operator securely embeds UA keypair and Cra into UA
(3.5) Registry adds HHIT and other info to DNS
(4) Croa and Cra are transmitted securely back to Operator/UA
(2) Operator sends, Caa and Coa to Registry

## Slide 18: tmrid: ua provisioning details
Operator typical near term will act on behalf of UA
  Separate but important issue of how to safely embed items generated by Operator into UA
EPP used to populate Registries then HIP RRs (HHIT, HI and RVS) and other information (using TXT records) are added to DNS
  What other information should be stored in DNS safely?
    Mostly self-certs (Coo, Caa, Crr) and Cra?
Registration involves giving UA a unique FQDN within the “.aero” domain
  Example: adamdrone.axenterprize.aero
  Could also use “random-value”.axenterprize.aero
    Only internally used, not necessarily required to be human usable?
    Combination of date/time and user public info (first name + make + registration date/time)?
  Forward DNS lookup: 1969fe9105d8629d.0014.0028[.4.2001002].[rid | remoteid].aero
  Reverse DNS lookup: need RRA and HDA on nibble boundaries to enable zone delegation
Open questions
  What information is held where and for how long?
  Should Cro be publicized in DNS?
    Stu – doesn’t hurt to put it in, validates hhit in hierarchy
  Does UA need either Croa and Coa?

## Slide 19: Certificate Details
Operator / UA
Coo = Sign{HIo(priv), HHITo + HIo + Expiration Timestamp}
  Stake unverified claim for HHITo
  116 bytes: sig(64) + hhit(16) + hi(32) + ets(4) = 116 bytes
Caa = Sign{HIa(priv), HHITa + HIa + Expiration Timestamp}
  Stake unverified claim for HHITa
  116 bytes: sig(64) + hhit(16) + hi(32) + ets(4) = 116 bytes
Coa = Sign{HIo(priv), Coo + Caa + Timestamp + Expiration Timestamp} (304 bytes)
  Assert binding between Operator and Aircraft
  304 bytes: sig(64) + coo(116) + caa(116) + ts(4) + ets(4) = 304 bytes
Registry
Crr = Sign{HIr(priv), HHITr + HIr + Expiration Timestamp} (116 bytes)
  ignores multi-level hierarchy for now
  Stake unverified claim for HHITr
  116 bytes: sig(64) + hhit(16) + hi(32) + ets(4) = 116 bytes
Cro = Sign{HIr(priv), Crr + Coo + Timestamp + Expiration Timestamp} (304 bytes)
  Assert Registry's blessing of Operator's desired HHIT
  held by operator as proof of registration of self (think like an issued drivers license)
  304 bytes: sig(64) + coo(116) + caa(116) + ts(4) + ets(4) = 304 bytes
Croa = Sign{HIr(priv), Cro + Coa + Timestamp + Expiration Timestamp} (680 bytes)
  Assert transitivity between Registry, Operator and Aircraft
  Held by Operator as proof of Registration of UA (think like an issued automobile registration)
  680 bytes: sig(64) + cro(304) + coa(304) + ts(4) + ets(4) = 680 bytes
Cra = Sign{HIr(priv), HHITr + Caa + Expiration Timestamp} (200 bytes)
  Asserts Registry's blessing of UA desired HHIT
  Exported to UA for use in tmrid Authentication message by UA itself
  200 bytes: sig(64) + hhit(16) + caa(116) + ets(4) = 200 bytes
Notes
  Sign { Private Key, Data}
  That Cxx Expiration Timestamp (ETS) is super long (most likely years).
  Cyx Timestamp and ETS MUST be no later than Cxx-ETS and Cyy-ETS
  To make Cra short (to fit in Auth message of Broadcast RID) we subbed HHITr for Crr. This allows for an attacker to attempt hash collision attacks on HHITr. This would require corrupting DNS. "Instead of robbing a bank, you are attempting to rob the banks bank."

## Slide 20
tmrid: message authentication w/o Internet
UA Broadcasts Cra and other messages (e.g. position + velocity) signed w/HIa(priv)
Observers verify signatures, ensuring received data (e.g. position track) all really came from UA w/claimed ID
Not Needed!
X
X

## Slide 21
tmrid: operator trust classification w/o Internet
Using small database on device (e.g., phone) listing only thousands of registries (not millions of UAS), Observer determines quadcopter is in general public registry & fixed wing in Observer trusted registry (of trusted operators) using broadcasted Cra of UA
Not Needed!
X

## Slide 22
tmrid: Observer to Operator or Pilot or Proxy (O2P2) comms
Observer w/credentials satisfying access control policy instantly establishes mutually authenticated, strongly encrypted comms w/pilot (e.g. to command exit from emergency UVR)
Steps:
(1) RID Bluetooth Broadcast
(2) DNS Query
(3) HIP Resource Record
(4) XACML Authorized RDAP Query
(5) Operator Personally Identifiable Information (PII)
(6,7) HIP sets up IPsec ESP Bound End-to-End Tunnel (BEET)
Pilot/Operator gets alert in web browser, accepts SIP VoIP call from Observer
(1)
(2)
(3)
(4)
(5)
(6)
(7)

## Slide 23
DNS: lookup of locator (IP address)
Steps:
DNS Query
A (or AAAA) RR provides IPv4 (or IPv6) address of Registry
(1)
(2)

## Slide 24
DNS + HIP: lookup & use of locator & identifier ([Hierarchical] Host Identity [Tag])
Steps:
DNS Query
HIP Resource Record
(3, 4) HIP mutually authenticates + optionally sets up secure tunnel
(1)
(2)
(3)
(4)

## Slide 25
whois: public registry lookup
Steps:
(1, 2) Operator registers domain name (e.g. adamsdrone.com)
(3, 4) Whois adamsdrone.com returns lots of PII to anyone (unless it is a private registration, which typically requires human contact & a search warrant)
(1, 2)
(1, 2)
(3, 4)
(3, 4)

## Slide 26
RDAP/XACML: access controlled registry lookup
(1, 2) Operator privately registers HHIT based domain name
(5, 6) Observer w/credentials not satisfying access control policy of this registration gets denied PII of Operator [XACML Request + Denial]
(3, 4) Observer w/credentials satisfying access control policy looks up PII of Operator [XACML Authorized RDAP Query + Response]
(1, 2)
(3, 4)
(5, 6)
(*)
Leverages protocols, infrastructure and business models of Internet domain name registration

## Slide 27
Crowd Sourced RID (CSRID):
Broadcast RID  Network RID Gateway & Multilateration
CSRID multilateration confirms UA2 RID position/velocity claims
CSRID multilateration disputes UA1 RID position/velocity claims: ALERT!

## Slide 28
(tm-rid) Interim 2010 FEB 06 THU:
Requirements Discussion
stu.card@axenterprize.com 315-725-7002
adam.wiethuechter@axenterprize.com
Substantive content additions/deletions/modifications or editorial comments?
https://datatracker.ietf.org/doc/draft-card-tmrid-uas-arch (not there yet, but soon!)