## Slide 1
Trustworthy Multipurpose Remote Identification
(tm-rid) Interim Webex 2010 FEB 06 THU:
Background & Requirements
Progress & Next Steps to add strong authentication techniques to identify physically nearby objects
Stu Card, Adam Wiethuechter

## Slide 2
Unmanned Aircraft System (UAS) Remote Identification (RID): Background
Need means to identify nearby observed Unmanned Aircraft (UA)
  complicated by small size, hi speed (relative to size), remote operation, autonomy…
Urgent
  EASA (EU) regulations already issued, become effective June 15 (check date)
  FAA (US) Notice of Proposed Rule Making (NPRM) comment period ends March 01
  Manufacturers will build to regs, locking in {good|bad} design for at least life of aircraft!
ASTM F38.02 WK65041 new standard: OpenDroneID messages / multi transports
  Network: from UAS (e.g. via LTE) or proxy (e.g. operator phone) via Internet to local observer phone
  Broadcast: Bluetooth 4 / 5 & WiFi beacons (short packets!) direct to observer phone [w/o Internet]
Initial ASTM standard falls short in making UAS RID information immediately actionable:
  trustworthy
  show whether operator is trusted, even if observer lacks Internet
  enable instant O2P2 & M2M secure comms, if endpoints have Internet
Aviators familiar w/radio comms, not networking; IETF could help
  leverage existing Internet services/infrastructure/protocols (e.g. WHOIS/RDAP, EPP, DNS, HIP)
  strengthen authentication, balance operator privacy w/genuine Need To Know
  generalize to support V2X, self-separation, collision avoidance
(UA physical location : UA ID) ~ (host logical location (IP) : host ID)
  we have prototyped & flown a HIP based extension to OpenDroneID @NY UAS Test Site

## Slide 3
Observing UA at a particular location, need to learn WHO (ID)
  Using that ID, observer can look up WHAT, WHY, “friendly”, etc.
Relevant for many entities for various reasons
  ATC, Public Safety Officials, Homeland Security, General Public, Private Security Personnel, Drone Operators...
  Vehicle to Infrastructure (V2I) + Vehicle to Vehicle (V2V) = V2X, C2, coordinated separation / collision avoidance, payload mission…
Trust begins with identity
  So identity needs to be trustworthy!
UAS RID is Critical for
UAS Traffic Management (UTM)

## Slide 4: Terminologies of the 2 worlds collide
UAS (ASTM & CAAs)
UA: Unmanned Aircraft
GCS: Ground Control Station
UAS: Unmanned Aircraft System (UA + GCS)
USS: UTM Service Supplier
SDSP: Supplemental Data Service Provider
UTM: UAS Traffic Management
UVR: UAS Volume Reservation
UAS RID: UAS Remote Identification
TMRID: Trustworthy Multipurpose Remote ID
Internet (IETF & ICANN)
DNS: Domain Name System
RR: Resource Record (in DNS)
WHOIS: domain name registry lookup tool
RDAP: Registry Data Access Protocol
EPP: Extensible Provisioning Protocol
HIP: Host Identity Protocol
[H]HI[T]: [Hierarchical] Host Identity [Tag]
Certificate: HHIT + HI, w/expiration, signed w/HI(priv)
  Cxy is a certificate signed by Entity X, attesting to the veracity of a claim made by Entity Y

## Slide 5: ASTM F38.02 WK65041 UAS RID
Focused on message formatting and performance in Remote ID
Broadcast RID
  Direct from UA to observer device (data link, not network)
  Bluetooth 4/5 & Wi-Fi w/Neighbor Awareness Networking (NAN)
    “selected for compatibility with commonly carried hand-held devices”
    BT4 Advertisement beacon payload limit of 25 bytes (24 usable)
  Broadcast always while in flight
Network RID
  Typically LTE
  Net-RID Service Provider (NETSP)
    UTM USS to which the UAS is subscribed
    Receives, stores & answers NETDP queries re: UAS ID, location, etc.
  Net-RID Display Providers (NETDP)
    Aggregates info from multi NETSP
    Provides picture of airspace volume in response to client queries
    May or may not itself be a USS
  Uses JSON and RestAPI to send information back and forth
Security methods punted to implementors, only framing specified

## Slide 6: FAA NPRM
Standard Remote ID
  Both Broadcast RID & Network RID required
  Both GCS (pilot) & UA locations transmitted
Limited Remote ID
  Small UA operating V-LOS within 400’ of pilot
  Network RID only (Broadcast prohibited)
  GCS location only (not UA)
Two ID types
  Manufacturer assigned Hardware Serial Number per ANSI/CTA-1063-A (ASTM UAS ID Type 1)
  UTM system assigned Session ID (ASTM UAS ID Type 3 UUID): “randomly-generated alphanumeric code that is used only for one flight” (p. 21, NPRM)

## Slide 7: FAA UAS Traffic Management (UTM) Pilot Project 2 (UPP2) Architecture

## Slide 8: UPP2 Use Case 4

## Slide 9: AXE UPP2 Use Case 5

## Slide 10: Difference between ASTM & NPRM
Overall they are intended to complement each other
  FAA rules mandate what must be done & performance requirements
  ASTM specifies an industry consensus technical means of compliance
Slightly different terminology
  NPRM “Remote ID USS” == ASTM “Net-RID Service Provider”
  NPRM “Session ID” == ASTM “UTM Assigned ID”
Message elements
  NPRM requires GCS location (longitude, latitude, pressure altitude)
    ASTM has most of these in optional messages (that can be required by CAA)
NPRM baseline is Network RID, ASTM baseline is Broadcast RID
  NPRM getting push-back on this esp. as EU allows Broadcast
  One or both will change
Integrity, security & privacy
  NPRM mandates error correction & “cybersecurity”
  ASTM specified only framing of authentication data, not auth methods
  Both give a nod to the idea that UAS operator privacy must be maintained if not forfeited by the UAS operator through clueless, careless or criminal actions

## Slide 11: Goal: Make RID Received Information Immediately Actionable -> Sub-Goals
make it trustworthy (despite severe constraints of Broadcast RID)
enable verification that an UAS is registered
  if so, in which registry (for classification of trusted operators on the basis of known registry vetting, even by observers lacking Internet connectivity at observation time)
enable instant establishment, by authorized parties, of secure communications with the remote pilot

## Slide 12: 1. tm-rid General Req’s for UAS
verify that messages originated from the claimed sender
verify that the UAS ID is in a registry & identify which one
lookup, from the UAS ID, public information
lookup, w/AAA, per policy, private information
structure information for both human and machine readability
provision registries with
  static information on the UAS & its Operator / Pilot In Command / Remote Pilot
  dynamic information on its current operation within the UTM
  Internet direct contact information for services related to the foregoing
close the AAA-policy registry loop by
  governing AAA per registered policies
  administering policies only via AAA
dynamically establish, w/AAA, per policy, E2E strongly encrypted communications w/the UAS RID sender & entities looked up from the UAS ID, inc. the GCS & USS
It is highly desirable that Broadcast RID receivers also be able to stamp messages with accurate date/time received and receiver location, then relay them to a network service (e.g. distributed ledger), inter alia for correlation to assess sender & receiver veracity.

## Slide 13: 2. tm-rid Req’s for UAS Identifiers
20 bytes or smaller
sufficient to identify a registry in which the UAS is listed
sufficient to enable lookup of other data in that registry
unique within a to-be-defined scope
non-spoofable within the context of Remote ID broadcast messages (some collection of messages provides proof of UA ownership of ID)
A tm-rid UAS ID MUST NOT facilitate adversarial correlation of UAS operational patterns; this may be accomplished e.g. by limiting each identifier to a single use, but if so, the UAS ID MUST support defined scalable timely registration methods.
Mechanisms standardized in tm-rid MUST be capable of proving ownership of a claimed UAS ID, and SHOULD be capable of doing so immediately on an observer device lacking Internet connectivity at the time of observation.
Mechanisms standardized in tm-rid MUST be capable of verifying that messages claiming to have been sent from a UAS with a given UAS ID indeed came from the claimed sender.

## Slide 14
(tm-rid) Interim 2010 FEB 06 THU:
Requirements Discussion
stu.card@axenterprize.com 315-725-7002
adam.wiethuechter@axenterprize.com
Substantive content additions/deletions/modifications or editorial comments?
https://datatracker.ietf.org/doc/draft-card-tmrid-uas-reqs