## Slide 1: IPv6 Options for DetNet
Author(s): Pascal Thubert ed., Yang Fan

## Slide 2: DetNet dataplane requirements served
Do not mix Flow (the water) and Path (the pipe)
Allow multiple flows and OAM with same treatment
Rich set of redundancy and path information
DetNet state in each node vs. inline (SRH) => path info is processed HbH
Not just sequence cnt, value using timestamp or opaque from ULP or LLP
Loose path information for slice / VRF / topology information
Early in the packet for hardware consumption
Extensible, e.g., coexistence with SRv6

## Slide 3: DetNet detailed requirements for IPv6
Redundancy Information for service sublayer
  Think sequence information but that’s too limitative
  No POF: Anything unique within the upper bound on out-of-order packet delivery
  If POF: Anything strictly ordered for the duration of the path, e.g., time stamp
  Network Coding: multiple fragments that can be delivered in any order
Path Information for both forwarding and service sublayer
  Path Information provides a scope for redundancy information
  DetNet places flows on paths need to signal that path in IPv6 Headers
  Same path  same DetNet treatment and fate share for all flows and OAM
  PREOF requires multipathing, not a linear sequence of nodes (terminology issue!)

## Slide 4: IPv6 HbH vs. Destination Option Header?
HbH
Path
Less Complexity in Dataplane
  6-tuple is a complex key to read and use, and may be lost in tunneling / crypto
  EH comes naturally with tunneling at PE if end-systems not service-aware
  The HbH EH is always first after the IPv6 Header: simpler P4 / ASIC processing
  e.g. Strict path, service sublayer distributed
  e.g. Strict path, service sublayer relay nodes indicated in SRH
IPv6 Header
HbH
Transport
header
…
payload
IPv6 Header
DOH
Transport
header
SRH
payload
Red.
Path
Red.

## Slide 5: Current version is 06
New: combines HbH with DOH + SRH
New: Example headers combos
DetNet Redundancy Information Option in HbH or DOH
  Sequence but but not only (e.g., time, include Net coding)
  Could be placed in DO if/when SRH signals service sublayer
DetNet Strict Path Option in HbH only
  DetNet forwarding layer is strict
DetNet Loose Path Option in HbH or DOH
  Clarifyed use, e.g., to signal Topology or slice

## Slide 6: Questions / Discussion

## Slide 7: A native IPv6 signaling for DetNet dataplane
The draft places the DetNet info in the IPv6 Extension Headers as OH
DetNet information available early in the packet and easy to grab
  HbH always comes first after IPv6 Hdr, DOH is before SRH if present
Signals the path and PHB independently of the transported flows
  Enables tunneling, OAM, and flow aggregation with common treatment
Fits IPv6 architecture to coexist with other IPv6 extensions e.g., SRv6
Fits DetNet architecture whereby edge nodes assign DetNet flows "to specific paths through a network“ [RFC 8655]

## Slide 8: Current version is 04
First personal submissions in quick sequence
  Early comments on applicability and option details
DetNet Redundancy Information Option
  Sequence but but not only (e.g., time, include Net coding)
  Could be placed in DO if/when SRH signals service sublayer
DetNet Strict Path Option
  DetNet forwarding layer is strict
DetNet Loose Path Option
  Relaxed to traverse non-service-aware
  Could/Should be fully replaced by SRH