## Slide 1: Requirements of large scale deterministic network
draft-du-detnet-layer3-low-latency-03
draft-geng-detnet-requirements-bounded-latency-03
Peng Liu liupengyjy@chinamobile.com
Zongpeng Du duzongpeng@chinamobile.com
Joanna Dang dangjuanna@huawei.com

## Slide 2: Different levels of application requirements
Critical SLAs - For “Industrial” networks
  Manufacture: Control/remote control-Cloud PLC
  Electricity: differential protection
Relatively lower levels of SLA- For “Consumer” networks
  Cloud gaming/Cloud VR
  Online meeting
Latency
Industrial, tight jitter, hard latency limit
Relatively lower levels latency requirement
Bets effort
Critical latency requirement
Industrial, hard latency limit

## Slide 3: Deployment and application status
TSN has been used in several industries
DetNet has done a lot of work and the standards are mature
Some trials of deterministic IP network has been done:
  Deterministic IP on CENI（3000 km and 13 hop devices, jitter<100 μs ）
  Remote control with Deterministic IP ( Cooperate with Baosteel, 600km, latency<=4ms, jitter <20us)
  Multi flows’ synchronization in an exhibition ( Cooperate with Emergen, Inter provincial)
  More work for network service providers to successfully sell DetNet type services to customers:
    Service Level objective definitions：absolute/relative latency/jitter/loss bounds, #flows, physcial scale, ...
    More option of queuing mechanisms for different service level
    Deployment considerations，such as integration into existing networks/service/controller-plane

## Slide 4: Requirements of technique in large scale deterministic network
Req1: tolerate a certain degree of time variance
  Synchronization
  Asynchronization
Req2: Consider the transmission latency
  300km/ms
Req3: Scalability
  a large number of network devices
  a massive number of traffic flows
Req4: Coexist with other traffic
Req5: Balance of cost and service requirements

## Slide 5: Req1: Tolerate a certain degree of time variance
Time Synchronization
  tolerate clock jitter & wander within a clock synchronous domain
  should support asynchronous clocks across domains(if in the scope)
Frequency Synchronization
  Network overhead of time Synchronization
  Accuracy
Asynchronization
  Not all the network or device support synchronization
  To be proved bounded latency to some extent(IEEE 802.1Qcr)

## Slide 6: Req2: Consider the transmission latency
The distance of transmission is long enough to generate a larger latency than a LAN
In particular, it will have an impact on queuing
Req3: Scalability
a large number of network devices
  For example, to connect so many 5G base stations
a massive number of traffic flows
  Flow aggregation needed

## Slide 7: Req4: Coexist with best-effort traffic
Req5: Balance of cost and service requirements
In the view of customers, dedicated network is the best network service(in fact maybe not)
Coexist with best-effort traffic can be an advantage of deterministic network
Whether to update all the network devices is the issue concerned by operators and related to the price concerned by customers
Some application that requires relatively lower levels of SLA may need simpler solution

## Slide 8: Proposed queuing mechanisms beside TSN and IntServ/GS ( Mechanisms not included in draft-ietf-detnet-bounded-latency)
If more queuing mechanisms could be proposed and be included in the scope of DetNet?
 | Mechanisms | Levels of deterministic | Synchronization | Update all the network device | Scalability | Flow aggregation
1 | draft-dang-queuing-with-multiple-cyclic-buffers/ draft-qiang-detnet-large-scale-detnet-05 | high | yes | yes | Good | Yes
2 | draft-du-detnet-layer3-low-latency-03 | medium | no | yes | Good | Yes
3 | draft-stein-srtsn-01 | ? | yes | yes | ? | ?
4 | draft-shi-quic-dtp-04 | low | ? | no | Good | no

## Slide 9
Thanks for listening
Welcome for comments