## Slide 1: Scheduling is not queuing
Yaakov (J) Stein
yaakovjstein@gmail.com
RAD
DetNet interim
13 Sept 2021

## Slide 2: What does a router (forwarder) do?
Forwarders perform 2 distinct per-packet and per-router* functions:
Forwarding — selecting to which output port a packet should be sent
Scheduling — selecting from which output queue
the next packet to be forwarded should be selected
Scheduling is therefore often called called queuing
* They may also perform per-flow or per-router functions, which are already handled well enough

## Slide 3: How has this changed?
When Segment Routing (or Traffic Engineering) is used
forwarding is more than simply selecting the correct output port
It involves deciding where the packet should be forwarded
When TSN/DetNet is used (i.e., when the network elements are synchronized)
scheduling is more than simply
selecting from which queue to forward
It involves deciding when to send any given packet
Such generalized scheduling may not involve any queues at all
Instead, it may employ any mechanism
that strives to send each packet at the right time

## Slide 4: Where in the IETF?
The right time has both control plane and user plane aspects
control (or management) plane
calculate the right time per packet per router
user (forwarding) plane
schedule each packet, optimally before its right time
and is hop-by-hop and not end-to-end
Such scheduling is hence unambiguously work for the RTG area
and not the TSV area
even disregarding my proposal
for combining scheduling with Segment Routing

## Slide 5: If not queues – then what?
A single queue is a First In First Out data structure
the packets in a queue are implicitly sorted by time of arrival
Multiple queues add a priority that is independent of time aspects
There are many alternatives to queue data structures, such as
the stack – a Last In First Out data structure
the sorted list – a linear data structure ordered by some field
the min (max) heap – a tree data structure in which
every parent node is < (>) its child nodes
In particular, draft-stein-srtsn proposes using
a stack of local deadlines in each packet
a sorted list or min heap data structure in the router
rather than queues!

## Slide 6: What can be done with a non-queue?
There are several known ways of using a sorted list or min heap
to reduce end-to-end propagation delay, for example :
Longest In System
  insert the packet's birth time into the header
  create sorted list or min heap based on birth times
  forward packets with earlier birth times before packets with later times
  this is suboptimal since a longer in system packet
  with a loose delay budget
  will be sent before a younger packet with a tight budget
Earliest Deadline First
  insert packet’s deadline into the header
  create sorted list or min heap based on deadline
  forward packets with earlier deadlines before packets with later deadlines
this is suboptimal since an EDF packet
already be near its destination
will be sent before a later packet far from its destination

## Slide 7: What is stack-based scheduling?
  With the stack-based approach
  insert a stack of local deadlines
  (with an entry for each router along the path) into the header
  create sorted list or min heap based on local deadline
  forward earlier deadline packets before packets with later times
This method has multiple advantages
the stack is inserted by the ingress router
which has its clock sync’ed to all the other routers
so that the local deadlines are directly comparable
it can be optimized even for relatively large networks
its configuration can be easily and rapidly distributed
new flows can be dynamically added or removed
it lowers average latency as compared to standard queueing
ratio of missed deadlines can be tuned

## Slide 8: What is SRTSN?
If we are already using a stack
why not reuse Segment Routing’s stack too?
In such case a single joint optimization
selects a path with appropriate immutable delay
calculates delay offsets for each router along that path
With SRTSN each time sensitive packet carries a stack with both
  forwarding (segment routing) instructions and
  scheduling (local deadline) instructions
in each stack entry

## Slide 9: Summary
With synchronized forwarding elements
scheduling means releasing packets at the right time
queues are not optimal data structures for scheduling
so scheduling is not queuing
optimal scheduling involves
  hop-by-hop and not end-to-end mechanisms
  a sophisticated control or management plane
  and is thus unambiguously work for RTG not TSV
inserting a stack of local deadlines into packet headers
conveys multiple advantages
combining deadline stacks with forwarding stacks
is even better

## Slide 10: Thanks for listening !
yaakovjstein@gmail.com