## Slide 1
LPWAN WG
WG Chairs:
Alexander Pelov <a@ackl.io>
Pascal Thubert <pthubert@cisco.com>
AD: Eric Vyncke
<evyncke@cisco.com>
Webex

## Slide 2: Note Well
This is a reminder of IETF policies in effect on various topics such as patents or code of conduct. It is only meant to point you in the right direction. Exceptions may apply. The IETF's patent policy and the definition of an IETF "contribution" and "participation" are set forth in BCP 79; please read it carefully.
As a reminder:
By participating in the IETF, you agree to follow IETF processes and policies.
If you are aware that any IETF contribution is covered by patents or patent applications that are owned or controlled by you or your sponsor, you must disclose that fact, or not participate in the discussion.
As a participant in or attendee to any IETF activity you acknowledge that written, audio, video, and photographic records of meetings may be made public.
Personal information that you provide to IETF will be handled in accordance with the IETF Privacy Statement.
As a participant or attendee, you agree to work respectfully with other participants; please contact the ombudsteam (https://www.ietf.org/contact/ombudsteam/) if you have questions or concerns about this.
Definitive information is in the documents listed below and other IETF BCPs. For advice, please talk to WG chairs or ADs:
BCP 9 (Internet Standards Process)
BCP 25 (Working Group processes)
BCP 25 (Anti-Harassment Procedures)
BCP 54 (Code of Conduct)
BCP 78 (Copyright)
BCP 79 (Patents, Participation)
https://www.ietf.org/privacy-policy/ (Privacy Policy)

## Slide 3
Reminder: Minutes are taken * This meeting might be recorded ** Presence is logged ***
* Please contribute to the minutes at: https://codimd.ietf.org/notes-ietf-interim-2021-lpwan-07-lpwan
** Recordings and Minutes are public and may be subject to discovery in the event of litigation.
*** From the Webex login

## Slide 4: Agenda bashing
[16:05] Administrivia [15min] o Note-Well, Scribes, Agenda Bashing
o WG Status, IETF 111 query
[16:20] SCHC Architecture [20min]
new version
[16:40] Data Model for SCHC [15min]
Yang Doctors feedback
[16:55] AOB [ QS ]

## Slide 5: WG Status

## Slide 6: Document advancement

## Slide 7: Action items
RFC 9011 published
  Congrats to the authors !!!!
draft-ietf-lpwan-coap-static-context-hc
  Soon too!!!
Nothing much else

## Slide 8: IETF 111
Meetings will be middle of the CEST night
  Or past that
We have interims
  5 interims
  Scheduled between now and then
Should we ask for an official meeting?

## Slide 9: draft-pelov-lpwan-architecture
Alexnader Pelov
Pascal Thubert
Ana Minaburo
Interim, May 4th, 2021

## Slide 10: Table of Contents
1. Introduction . . . . . . . . . . . . . . . . . . . . . . . . 2
2. LPWAN Technologies and Profiles . . . . . . . . . . . . . . . 2
3. The Static Context Header Compression . . . . . . . . . . . . 3
4. SCHC Endpoints . . . . . . . . . . . . . . . . . . . . . . . 3
5. SCHC Instances . . . . . . . . . . . . . . . . . . . . . . . 4
6. SCHC Data Model . . . . . . . . . . . . . . . . . . . . . . . 5
7. Security Considerations . . . . . . . . . . . . . . . . . . . 7
8. IANA Consideration . . . . . . . . . . . . . . . . . . . . . 7
9. Acknowledgements . . . . . . . . . . . . . . . . . . . . . . 7
10. References . . . . . . . . . . . . . . . . . . . . . . . . . 7

## Slide 11: LPWAN Technologies and Profiles
Discusses RFC 8376, the LPWAN technologies
Points on appendix D of RFC 8724
RFC 9011 as an example

## Slide 12: The Static Context Header Compression
Discusses RFC 8724, SCHC
C/D , parser
ruleID
F/R

## Slide 13: SCHC Endpoints
DEVice / NGW model
() () () |
() () () () / \ +---------+
() () () () () () / \======| ^ | +-----------+
() () () | | <--|--> | |Application|
() () () () / \==========| v |=============| Server |
() () () / \ +---------+ +-----------+
Dev RGWs NGW App
Figure 1: Typical LPWAN Network Architecture
vs. Peer to Peer
+----------+ Wi-Fi / +----------+ ....
| IP | Ethernet | IP | .. )
| Host +-----/------+ Router +----------( Internet )
| SCHC C/D | Serial | SCHC C/D | ( )
+----------+ +----------+ ...
<-- SCHC -->
over PPP
Figure 2: PPP-based SCHC Deployment

## Slide 14: SCHC Instances
Different endpoints, different nodes
(device) (NGW) (App)
+--------+ +--------+
A S | CoAP | | CoAP |
p C | inner | | inner |
p H +--------+ +--------+
. C | SCHC | | SCHC |
| inner | cryptographical boundary | inner |
-._.-._.-._.-._.-._.-._.-._.-._.-._.-._.-._.-._.-._.-._.-._.-._.-._.-._
A S | CoAP | | CoAP |
p C | outer | | outer |
p H +--------+ +--------+
. C | SCHC | | SCHC |
| outer | layer / functional boundary | outer |
-._.-._.-._.-._.-._.-._.-._.-._.-._.-._.-._.-._.-._.-._.-._.-._.-._.-._
N . UDP . . UDP .
e .......... .................. ..........
t . IPv6 . . IPv6 . . IPv6 .
w S .......... .................. ..........
o C . SCHC . . SCHC . . . .
r H .......... .......... . . .
k C . LPWAN . . LPWAN . . . .
.......... .................. ..........
((((LPWAN)))) ------ Internet ------

## Slide 15: SCHC Data Model
Same rules deployed on both side
(-------) (-------)
( Rules ) ( Rules )
(-------) (-------)
. read . read
. .
+-------+ +-------+
<===| R & D |<=== <===| C & F |<===
===>| C & F |===> ===>| R & D |===>
+-------+ +-------+
Allows deployment / configuration through NETCONF, RESTCONF, and CORECONF
create
(-------) read +=======+ *
( rules )<------->|Rule |<--|-------->
(-------) update |Manager| NETCONF, RESTCONF or CORECONF
. read delete +=======+ request
.
+-------+
<===| R & D |<===
===>| C & F |===>
+-------+

## Slide 16: Security Considerations
Need to protect the rule distribution
What else?

## Slide 17: Missing Topics / Content?
Any coauthors to work on this?
Do we want/need applicability statements in this document?
Anything else needs to be on the document?
E.g., Applicability
  In Smart Building, smart grid?
  e.g., Goose (?) protocol. Very chatty, long name strings.
  Would love to SCHC-compress it.

## Slide 18: Next steps
Adoption call
Like Now ?

## Slide 19: draft-ietf-lpwan-schc-yang-data-model-04
Laurent Toutain (laurent.toutain@imt-atlantique.fr)
Ana Minaburo (ana@ackl.io)

## Slide 20: YANG doctor review
Many thanks to Carl Moberg
  Very good remarks to make a better document
Presentation: pyang -m yang
IETF compatibility: pyang --ietf
New model version on github:
  https://github.com/lp-wan/datamodel/blob/master/ietf-schc%402021-04-23.yang

## Slide 21: Changes
Module name: ietf-schc
Version: 1.1
As is right now, the YANG module assumes that all implementations support all FID types defined to be derived from field-id-base-type. It includes fields related IPv6, COAP/OSCORE, and ICMPv6 all in the same module.
Is there a possibility that some implementations won't implement all three of those protocol groups? If so, it might be worth considering making FID type groups either optional using YANG 'feature' statements or break them out into separate modules to be advertised separately.
Hierarchical FID
  A type for each protocol IPv6, UDP, CoAP, ICMPv6
  A sub-type for sub-fields

## Slide 22: Field-id

## Slide 23: Relation between fields
“does the authors think it important (and possible) to work towards a more stringent validation of "meaningful" configuration by capturing the relationships between fields like in this example?”
  The current YANG permits a field-identifier 'fid-ipv6-version' combined with a field-length 'fl-token-length' in a rule entry, which I understand to be nonsensical.
  TV is mandatory for MO equal, MSB and match-mapping
  Window size in mandatory for AA and equal 1, any size for AoE,
  No Window for NoAck
  ????

## Slide 24
?????
Syntax

## Slide 25
AOB ?