## Slide 1: A DODAG Metric Used for DODAG Selection in LLNs
Huimin She (hushe@cisco.com)
Li Zhao (liz3@cisco.com)
Pascal Thubert (pthubert@cisco.com)

## Slide 2: Motivation
LLNs consists of a border router (root) and nodes
  Limited nodes managed by a root
  Load balance
Which DODAG to join for a new node?
  Already exist: Link ETX
  Missing: DODAG size
root
root
Which PAN
to join?

## Slide 3: RFC6550: DAG metric container
RFC 6550: DAG metric Container Option
  report metrics along the DODAG

## Slide 4: RFC6551: DAG metric container
RFC 6551: Routing Metric/Constraint Object Generic Format

## Slide 5: DODAG size object
DODAG size object format
  Extends RFC 6551
8 bits | 5 | 1 | 1 | 1 | 1 | 3 | 4 | 8 | 16
Type | Res Flags | P | C | O | R | A | Prec | Length (bytes) | DODAG size
Type: 9 (suggested)
Flags:
  P = 0, C = 0, O = 0, R = 1, A = 0
  Prec: useful when a DAG Metric Container contains several Routing Metric objects. Its value ranges from 0 to 15. The value 0 means the highest precedence.
  Length: 2

## Slide 6: Disseminate DODAG Size
DODAG size
  Collected by the root
  Periodically disseminated to nodes in the PAN
Two ways to disseminate DODAG Size
  DIO
  DAO-ACK