## Slide 1: Root initiated routing state in RPL
Pascal Thubert
draft-ietf-roll-dao-projection
Interim Jan. 2021
ROLL Virtual Meeting
P. Thubert, Ed.; R.A. Jadhav, M. Gillmore

## Slide 2: Status to the draft
Published -15 and -16 since last IETF
Non-Storing Mode SRH may be loose
Main DODAG MUST be Non-Storing Mode
Track <=> Non-Storing Mode main DODAG:
  Root is Track Ingress,
  Signaled by one or more Non-Storing-Mode P-DAO messages
  Track Ingress encapsulates external packets (as in useofrplinfo)
  Track Ingress places the SRH in the packet in source routed tracks
  There cannot be non-storing segments (only Tracks withing Tracks)
Storing Mode P-DAO signals Segment of a Track or of main DODAG
  Does not need re-encapsulation
  Unless implicit Track => Do we support that ?
Interim 1/2021 - ROLL

## Slide 3: Status to the draft (cont)
RPI modified to indicate P-Route
Extending RFC 6553 and RFC 8138
  0 1 2
  0 1 2 3 4 5 6 7 8 9 0 1 2 3 4 5 6 7 8 9 0 1 2 3
  +-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+
  |1|0|E| Length | 6LoRH Type 7 | RPLInstanceID |
+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+
New P-RPI-6LoRH, both elective and non-elective forms
Interim 1/2021 - ROLL

## Slide 4: Encapsulation Rules
Source of outer header MUST be Track Ingress
RPL Instance ID in RPI MUST indicate TrackID (if not main DODAG)
SR-VIO: Loose from Track Ingress, excluded, to Egress, included
  Copied Verbatim in inserted SRH-6LoRH,
  Requires encapsulation (can be recursive)
SF-VIO: Strict from Segment Ingress to Egress, both included
  No Encapsulation if Source and RPI both match Segment definition
  A Segment is an Implicit Track if P-DAO Ingress == 1st SF-VIO entry
TBD: matching rules, Flow Info option, when to tunnel?

## Slide 5: P-DAO construction
RPL Target Options can be factorized
But there is one and only one VIO (SF-VIO or SR-VIO)
So the Ack management is easier
VIO sent to egress; SR-VIO sent to ingress
Track ID is a RPL local instance ID
Taken from the Track Egress Name Space

## Slide 6: P-DAO Format
0 1 2 3
0 1 2 3 4 5 6 7 8 9 0 1 2 3 4 5 6 7 8 9 0 1 2 3 4 5 6 7 8 9 0 1
+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+
| Type | Option Length | Flags | SegmentID |
+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+
|Segm. Sequence | Seg. Lifetime | SRH-6LoRH header |
+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+
| |
+ +
. .
. Via Address 1 .
. .
+ +
| |
+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+
| |
. .... .
| |
+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+
| |
+ +
. .
. Via Address n .
. .
+ +
| |
+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+
Must be optimized in Non-storing Mode, to be used as is in packets
May be more than one in Non-storing Mode

## Slide 7: Topology awareness
Initially out of scope
Now we have non storing mode + Sibling info option
  Acronym conflict with RPL’s Solicited Information Option
Which sibling to advertise is still out of scope
  Separate draft?
Interim 1/2021 - ROLL

## Slide 8: Profile 1: Compress SRH in main DODAG with strict SM Segments
Main DODAG Root
Loose Hop 3 = E
Loose hop 2 = C
P-DAO 1
Loose SRH = A, C, E, F
Loose hop 1 = A
Dest = F
SRC=Root
TrackID=0
P-DAO 1
A
D
F
P-DAO 2
B
C
E
Ingress=Root
TrackID=0
SF-VIO =A, B
Target =B, C
Ingress=Root
TrackID=0
SF-VIO =C, D, E
Target = E
2 ways of saying roughly the same thing
Should hops in SF-VIO be implicit targets?
Segment 1
Segmt 2
2
P-DAO 1
1
ACK 2

## Slide 9: Profile 2: Compress SRH in main DODAG with Strict NSM Tracks
Main DODAG Root
Loose Hop 3 = E
Loose hop 2 = C
P-DAO 1
Loose SRH = A, C, E, F
Loose hop 1 = A
Dest = F
SRC=Root
TrackID=0
A
D
F
P-DAO 2
B
C
E
Ingress=A
TrackID=(A, 129)
SR-VIO =B
Target =C
Ingress=C
TrackID=(C, 131)
SR-VIO =D, E
Target =
2 ways of saying roughly the same thing
Last hop (Egress) in SR-VIO is implicit target
Track 2
Track 1
ACK 2
A 1

## Slide 10: Profile 3: Implicit Track with Strict SM Segments,
External node S
Implicit Egress = E
Dest = F
SRC=A
TrackID=129
A
D
F
B
C
E
Ingress=A
TrackID=129
SF-VIO = A,B,C,D,E
Target = E,F
The track is Implicit
Can we inject packets along?
Segment 1
P-DAO 1
ACK 1
Src=S, Dst=F
Src=S, Dst=F
Dest = E
Implicit Ingress = A
P-DAO 1
P-DAO 1
P-DAO 1
P-DAO 1
Need Sibling Information

## Slide 11: Profile 4: Strict NSM Explicit Track
External node S
Egress = E
Ingress = A
Dest = F
SRC=A
TrackID=129
A
D
F
B
C
E
Ingress=A
TrackID=129
SR-VIO = B,C,D,E
Target = F
The track is Explicit
Track 1
P-DAO 1
Src=S, Dst=F
Src=S, Dst=F
Dest = C
SRH = D, E
Loose hop 2 = C
Loose hop 3 = D
Loose hop 1 = B
Need Sibling Information
ACK 1

## Slide 12: Profile 5: Compress SRH in Track with Strict SM Segments
External node S
Loose Hop 3 = E
Loose hop 2 = C
P-DAO 1
Src= A, RPI=129
Track Ingress A
Dest = F
Src=S, Dst=F
P-DAO 1
S
D
G
P-DAO 2
B
C
E
Ingress=A
TrackID=(A, 129)
SF-VIO =A, B
Target =B, C
Ingress=I
TrackID=(A, 129)
SF-VIO =C, D, E
Target = E
Same as Profile 1, but for Track
Segment 1
Segmt 2
P-DAO 3
Ingress=A
TrackID=(A, 129)
SR-VIO =C, E
Target = F
A
Dest = C
SRH = E
Src= A, RPI=129
Dest = E
SRH consumed
F
Src=S, Dst=F
Need Sibling Information
3
2
1
2
1

## Slide 13: Profile 6: Compress SRH in Track with NSM Tracks (Recursive?)
External node S
Loose Hop 3 = E
Loose hop 2 = C
Loose hop 1 = A
Dest = F
I
D
F
B
C
E
Tunnel within Tunnel
P-DAO 3
Ingress=A
TrackID=(A, 141)
SR-VIO =C, E
Target = F
A
P-DAO 1
P-DAO 2
Ingress=A
TrackID=(A, 129)
SR-VIO =B
Target =C
Ingress=C
TrackID=(C, 131)
SR-VIO =D, E
Target =
Track 2
Track 1
Src= A, RPI=141
Dest = C
SRH = E
Src= A, RPI=129
Dest = B
Src=S, Dst=F
Src=S, Dst=F

## Slide 14: Huimin’s comments / suggestions
Lifetime unit: ReqLifetime, Track lifetime, and Segment Lifetime are defined as 8 bits. And their lifetime Unit is obtained from the DODAG configuration option. It will lead to inflexibility as all tracks in the PAN use the same lifetime unit. We propose to define lifetime unit separately for each track ( for example adding a 2-bit flag to indicate second, minute, hour, day). Details can be discussed later.
Now the TrackID has the same meaning as Local RplInstanceID. How does a node judge whether the received message is a P-DAO message or Local RPL instance DAO message? Is it possible to define a flag in the P-DAO message?
The P-DAO track/segment is single-directional. I suggest to add the possibility for creating bi-directional segments/tracks. We can add a flag in the PDR message to indicate the requested track is single-directional or bi-directional.
I suggest to add a flow of message exchanges for “PDR, PDR-ACK, P-DAO, P-DAO ACK” in the draft.

## Slide 15: Other to be done
Loop avoidance
Who sends PDR? If it was destination, then it could select the trackID from its name space
ND (RFC 8505) to maintain sibling neighbor state
Be very specific if Ingress and Egress are listed in RPOs
  Ingress to indicate which source address to use
  Egress to build the full SRH 6LoRH

## Slide 16: BAckup