## Slide 1: Root initiated routing state in RPL
Pascal Thubert
draft-ietf-roll-dao-projection
Interim Aug. 2021
ROLL Virtual Meeting
P. Thubert, Ed.; R.A. Jadhav, M. Gillmore

## Slide 2: Status to the draft
Published -17 to -19 since last interim
Sibling address in SIO based on RFC 8505 discovery
Simplification: PDR always from Track Ingress, which provides TrackID
Clarification on maintenance: how to repair Track Segments (storing mode) and Legs (non-Storing e2e)
Clarification: Policies to inject traffic on Tracks is OOS
Reviews by S.V.R. Anand and Toerless (in progress)
Interim 1/2021 - ROLL

## Slide 3: On Maintenance (Anand’s review)
interference
Anand’s point on making the connectivity to the root more reliable.
No-Path P-DAO indicated by lifetime of 0
Can indicate a section of a Segment
Updating can be lossless but possible misordering; e.g.:
Interim 1/2021 - ROLL
B
C
D
G
H
E
A
F

## Slide 4
Interim 1/2021 - ROLL
B
C
D
G
H
E
A
F
SF VIO= (G, F, E, C)
B
C
D
G
H
E
A
F
B
C
D
G
H
E
A
F
DAO Ack
B
C
D
G
H
E
A
F
SF VIO= (D)
Lifetime=0

## Slide 5: On Track
A Track is a RPL local instance installed by P DAO.
Goal: to be equivalent to Non-Storing Mode main DODAG
The spec only builds multi-legged Tracks (parallel or crossing)
  Root is Track Ingress, Root address + DODAGID identify the Track
  A Leg is signaled by a Non-Storing-Mode P-DAO message
  Track Ingress encapsulates external packets (as in useofrplinfo)
  Track Ingress places the SRH in the packet in source routed tracks
  There cannot be non-storing segments (only Tracks within Tracks)
Storing Mode P-DAO signals Segment of a Track or of main DODAG
  Does not need re-encapsulation
  Unless implicit Track => Do we support that ?
Interim 1/2021 - ROLL

## Slide 6: Discussion: building real DODAGs
With -19, a complex track is multi-legged, e.g., 2 Legs below
Allows 1+n
Main DODAG Root
Loose Hop 3 = I
Loose hop 2 = H
Loose hop 1 = G
Dest = F
Segment 4
Segmt 3
Loose Hop 3 = E
Loose hop 2 = C
Loose hop 1 = A
Segment 1
Segmt 2
One Leg

## Slide 7: Discussion: building real DODAGs
NO North-South Segment
Main DODAG Root
Loose Hop 3 = I
Loose hop 2 = H
Loose hop 1 = G
Dest = F
Segment 4
Segmt 3
Loose Hop 3 = E
Loose hop 2 = C
Loose hop 1 = A
Segment 1
Segmt 2
Not intended

## Slide 8: Discussion: How to do this?
Proposal: use RFC 6550 non-storing Target and Transit to indicate loose parent child relationship, many of them in one P-DAO
Main DODAG Root
Loose Hop 3 = I
Loose hop 2 = H
Loose hop 1 = G
Dest = F
Loose Hop 3 = E
Loose hop 2 = C
Loose hop 1 = A
Segment 4
Segmt 3
Segment 1
Segmt 2
Segment 8
Segmt 6
Segment 7
Segmt 5

## Slide 9: Proposal on the table: building real DODAGs
Allow the root to pack 1*(1*target 1*transit) in P_DAO
Provides the Ingress similar information to what a main Root has in non storing mode
Ingress makes same computations as main Root and gets the instance topology as a DODAG.
Interim 1/2021 - ROLL

## Slide 10: Slides from previous meetings

## Slide 11: Status to the draft (cont)
RPI modified to indicate P-Route
Extending RFC 6553 and RFC 8138
  0 1 2
  0 1 2 3 4 5 6 7 8 9 0 1 2 3 4 5 6 7 8 9 0 1 2 3
  +-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+
  |1|0|E| Length | 6LoRH Type 7 | RPLInstanceID |
+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+
New P-RPI-6LoRH, both elective and non-elective forms
Interim 1/2021 - ROLL

## Slide 12: Encapsulation Rules
Source of outer header MUST be Track Ingress- think DODAG Root
RPL Instance ID in RPI MUST indicate TrackID (if not main DODAG)
SR-VIO: Loose from Track Ingress, excluded, to Egress, included
  Copied Verbatim in inserted SRH-6LoRH,
  Requires encapsulation (can be recursive)
SF-VIO: Strict from Segment Ingress to Egress, both included
  No Encapsulation if Source and RPI both match Segment definition
  A Segment is an Implicit Track if P-DAO Ingress == 1st SF-VIO entry
TBD: matching rules, Flow Info option, when to tunnel?

## Slide 13: P-DAO construction
RPL Target Options can be factorized
But there is one and only one VIO (SF-VIO or SR-VIO)
So the Ack management is easier
VIO sent to egress; SR-VIO sent to ingress
Track ID is a RPL local instance ID
Taken from the Track Egress Name Space

## Slide 14: P-DAO Format
0 1 2 3
0 1 2 3 4 5 6 7 8 9 0 1 2 3 4 5 6 7 8 9 0 1 2 3 4 5 6 7 8 9 0 1
+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+
| Type | Option Length | Flags | SegmentID |
+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+
|Segm. Sequence | Seg. Lifetime | SRH-6LoRH header |
+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+
| |
+ +
. .
. Via Address 1 .
. .
+ +
| |
+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+
| |
. .... .
| |
+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+
| |
+ +
. .
. Via Address n .
. .
+ +
| |
+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+
Must be optimized in Non-storing Mode, to be used as is in packets
May be more than one in Non-storing Mode

## Slide 15: Topology awareness
Initially out of scope
Now we have non storing mode + Sibling info option
  Acronym conflict with RPL’s Solicited Information Option
Needed for profiles >= 3
Which sibling to advertise is still out of scope
  Separate draft?
Interim 1/2021 - ROLL

## Slide 16: Profile 1: Compress SRH in main DODAG with strict SM Segments
Main DODAG Root
Loose Hop 3 = E
Loose hop 2 = C
P-DAO 1
Loose SRH = A, C, E, F
Loose hop 1 = A
Dest = F
SRC=Root
TrackID=0
P-DAO 1
A
D
F
P-DAO 2
B
C
E
Ingress=Root
TrackID=0
SF-VIO =A, B
Target =B, C
Ingress=Root
TrackID=0
SF-VIO =C, D, E
Target = E
2 ways of saying roughly the same thing
Should hops in SF-VIO be implicit targets?
Segment 1
Segmt 2
2
P-DAO 1
1
ACK 2

## Slide 17: Profile 2: Compress SRH in main DODAG with Strict NSM Tracks
Main DODAG Root
Loose Hop 3 = E
Loose hop 2 = C
P-DAO 1
Loose SRH = A, C, E, F
Loose hop 1 = A
Dest = F
SRC=Root
TrackID=0
A
D
F
P-DAO 2
B
C
E
Ingress=A
TrackID=(A, 129)
SR-VIO =B
Target =C
Ingress=C
TrackID=(C, 131)
SR-VIO =D, E
Target =
2 ways of saying roughly the same thing
Last hop (Egress) in SR-VIO is implicit target
Track 2
Track 1
ACK 2
A 1

## Slide 18: Profile 3: Implicit Track with Strict SM Segments,
External node S
Implicit Egress = E
Dest = F
SRC=A
TrackID=129
A
D
F
B
C
E
Ingress=A
TrackID=129
SF-VIO = A,B,C,D,E
Target = E,F
The track is Implicit
Can we inject packets along?
Segment 1
P-DAO 1
ACK 1
Src=S, Dst=F
RPI = 0
Src=S, Dst=F
Dest = E
Implicit Ingress = A
P-DAO 1
P-DAO 1
P-DAO 1
P-DAO 1
Need Sibling Information

## Slide 19: Profile 4: Strict NSM Explicit Track
External node S
Egress = E
Ingress = A
Dest = F
SRC=A
TrackID=129
A
D
F
B
C
E
Ingress=A
TrackID=129
SR-VIO = B,C,D,E
Target = F
The track is Explicit
Same encap as profile 2
Track 1
P-DAO 1
Src=S, Dst=F
Src=S, Dst=F
Dest = C
SRH = D, E
Loose hop 2 = C
Loose hop 3 = D
Loose hop 1 = B
Need Sibling Information
ACK 1

## Slide 20: Profile 5: Compress SRH in Track with Strict SM Segments
External node S
Loose Hop 3 = E
Loose hop 2 = C
P-DAO 1
Src= A, RPI=129
Track Ingress A
Dest = F
Src=S, Dst=F
P-DAO 1
S
D
G
P-DAO 2
B
C
E
Ingress=A
TrackID=(A, 129)
SF-VIO =A, B
Target =B, C
Ingress=A
TrackID=(A, 129)
SF-VIO =C, D, E
Target = E
Same as Profile 1, but for Track
Segment 1
Segmt 2
P-DAO 3
Ingress=A
TrackID=(A, 129)
SR-VIO =C, E
Target = F
A
Dest = C
SRH = E
Src= A, RPI=129
Dest = E
SRH consumed
F
Src=S, Dst=F
Need Sibling Information
3
2
1
2
1

## Slide 21: Profile 6: Compress SRH in Track with NSM Tracks (Recursive?)
External node S
Loose Hop 3 = E
Loose hop 2 = C
Loose hop 1 = A
Dest = F
I
D
F
B
C
E
Tunnel within Tunnel
P-DAO 3
Ingress=A
TrackID=(A, 141)
SR-VIO =C, E
Target = F
A
P-DAO 1
P-DAO 2
Ingress=A
TrackID=(A, 129)
SR-VIO =B
Target =C
Ingress=C
TrackID=(C, 131)
SR-VIO =D, E
Target =
Track 2
Track 1
Src= A, RPI=141
Dest = C
SRH = E
Src= A, RPI=129
Dest = B
Src=S, Dst=F
Src=S, Dst=F

## Slide 22: Huimin’s comments / suggestions
Lifetime unit: ReqLifetime, Track lifetime, and Segment Lifetime are defined as 8 bits. And their lifetime Unit is obtained from the DODAG configuration option. It will lead to inflexibility as all tracks in the PAN use the same lifetime unit. We propose to define lifetime unit separately for each track ( for example adding a 2-bit flag to indicate second, minute, hour, day). Details can be discussed later.
Now the TrackID has the same meaning as Local RplInstanceID. How does a node judge whether the received message is a P-DAO message or Local RPL instance DAO message? Is it possible to define a flag in the P-DAO message?
The P-DAO track/segment is single-directional. I suggest to add the possibility for creating bi-directional segments/tracks. We can add a flag in the PDR message to indicate the requested track is single-directional or bi-directional.
I suggest to add a flow of message exchanges for “PDR, PDR-ACK, P-DAO, P-DAO ACK” in the draft.

## Slide 23: Other to be done
Loop avoidance
Who sends PDR? If it was destination, then it could select the trackID from its name space
ND (RFC 8505) to maintain sibling neighbor state
Be very specific if Ingress and Egress are listed in VIOs
  Ingress to indicate which source address to use
  Egress to build the full SRH 6LoRH

## Slide 24: BAckup