## Slide 1: draft-ietf-stir-certificates-ocsp draft-peterson-stir-certificates-shortlived
IETF 113i (virtual)
STIR WG
Jon

## Slide 2: Who Cares about Freshness?
This is a rerun from IETF 98 (!)
Freshness is different for STIR certs than regular PKI certs
  This is due to TNAuthList
    Not for SPCs, really, just for TNs
  The problem is the inherent dynamism of number assignment
    Relying parties want to know if a cert is still valid for a number right now
So why are these back on the menu?
  Because of certificate delegation, and the use of TN’s by-reference in delegate certs especially
  Need a way to verify that a particular number is valid for a cert that does not involve downloading an entire TNAuthList

## Slide 3: Two paths
Refreshed some ancient drafts: OCSP and short-lived certs
  They have very different privacy properties, potentially
Basically, I propose we explore both paths a bit and see what the experience yields
  Still (!) – because the drafts have been updated to be about the TN use of TNAuthList for certificate delegation in particular
  Not intended to compete with any CRLs for SPC use of TNAuthList, be they centralized or federated

## Slide 4: Real-time Credential Validation
Inter-
Mediary
PBX
Endpoint
User
Endpoint
User
Endpoint
User Endpoint
Logical
Authority
Unsigned
Requests
Inter-
Mediary
PBX
Endpoint
User
Endpoint
User
Endpoint
Credential
Provisioning
(infrequent)
Credential
Validation
(OCSP)
Signed
Requests (rfc4474bis + PASSporT)
Same architecture with
either approach

## Slide 5: The OCSP Path
Two ways: either terminating side or stapled
  Terminating side is where much of the privacy leak occurs
Probably, we would recommend stapling
  We would define a SIP header for carrying a staple
    Probably a general SIP feature, actually, not just for STIR
  Staple basically says “the cert is valid for this number right now”
The properties of stapling and short-lived certs start to look real, real similar

## Slide 6: Stapled Validation
Inter-
Mediary
PBX
Endpoint
User
Endpoint
User
Endpoint
User Endpoint
Logical
Authority
Unsigned
Requests
Inter-
Mediary
PBX
Endpoint
User
Endpoint
User
Endpoint
Credential
Stapling
(shortlived)
Signed
Requests (rfc4474bis + PASSporT)
Same architecture with
either approach

## Slide 7: Short-lived Credentials
Inter-
Mediary
PBX
Endpoint
User
Endpoint
User
Endpoint
User Endpoint
Logical
Authority
Unsigned
Requests
Inter-
Mediary
PBX
Endpoint
User
Endpoint
User
Endpoint
Credential
Provisioning
(shortlived)
Signed
Requests (rfc4474bis + PASSporT)
Same architecture with
either approach

## Slide 8: Short-lived
Issuing certs that expire soon
  Could be for individual numbers even (or ranges)
  Basically says, “this cert is valid for this number right now”
    Also obviates the need for relying parties to talk to the CA
What does short-lived mean?
  Hours? Days? Not months or years anyway.
  Part of our job is to decide what is appropriate
The hard part is getting the new cert… but...

## Slide 9: ACME makes short-lived easy
Proof
ACME
Client
Certificate
Authority
Certificate
Provisioning
Proofing
Relying
Party
Validate
Communication

## Slide 10: Individual TN certs: not just for end users
ACME allows CSPs that control large number blocks to use disposable, single-number certs
  A CSP basically uses an ACME “account” to get certs issued for numbers under its control as needed
  Relying parties only know that the cert attests a number – doesn’t reveal the SPC unless you want to
  Might be useful for some SHAKEN-like environments
Similar mechanisms could work for enterprises
Solves privacy concerns without requiring new protocol work for OCSP, new staple header, etc.

## Slide 11: So what to do?
I (still) say let’s explore both a bit, see which story is better
Not much harm in kicking the tires on both approaches out there in implementation
  In fact, they aren’t really incompatible, both could coexist in the marketplace
Should we advance either/both?