## Slide 1
TSN Queuing Mechanisms Evaluation
Yufang Han ZTE Corporation
Shaofu Peng ZTE Corporation
Yuehong Gao Beijing University of Posts and Telecommunic

## Slide 2
01
Motivation
Identify the points where these TSN queuing mechanisms do not meet the requirements and need to be enhanced, providing reference information for new queuing mechanisms.
Verify the rationality and necessity of requirements through evaluation, in order to clarify and improve the requirements draft.
Use the requirement draft to evaluate the new proposed queuing mechanisms.

## Slide 3
03
TAS Evaluation
section | Requirements | Evaluation | Notes
3.1 | Tolerate Time Asynchrony | No | All terminals and network devices need to achieve nanosecond clock synchronization, to ensure that the GCL time of all outgoing ports is synchronized.
3.2 | Support Large Single-hop Propagation Latency | Yes | Link delay is naturely cosidered during GCL calculation. GCL is independently installed on each node.
3.3 | Accommodate the Higher Link Speed | Partial | More precise time control (smaller TimeInterval of GCL) is required.
3.4(1) | Be Scalable to the Large Number of Flows | Partial | GCL calculation for all flows in the control plane is NP-hard problem. Maintian queues per traffic class. TAS does not restrict the strategy of flow entering traffic class based queues.
3.4(2) | Tolerate High Utilization | Partial | The TimeInterval of GCL, with dedicated bandwidth, reserved for a TSN flow is exclusive. If that TSN flow does not send packets, the bandwidth is waste.
3.5 | Prevent Flow Fluctuation from Disrupting Service | No | The re-calculation of the GCLs are more complicated and requires to update GCLs frequently.
3.6 | Tolerate Failures of Links or Nodes and Topology Changes |  | Not related to queuing mechanisms directly.
3.7 | Be Scalable to a Large Number of Hops with Complex Topology | Partial | More complexity of GCL calculations due to NP-hard problem. E2E queueing delay is negligible. E2E delay jitter is ultra-low.
3.8 | Support Multi-Mechanisms in Single Domain and Multi-Domains |  | Not related to a single queuing mechanism directly.
TAS (Time-Aware Shaper), refer to IEEE 802.1Qbv

## Slide 4
02
CBS Evaluation
section | Requirements | Evaluation | Notes
3.1 | Tolerate Time Asynchrony | Yes | Does not rely on time synchronization or frequency synchronization.
3.2 | Support Large Single-hop Propagation Latency | Yes | Link delay does not affect the rate based shaping logic of CBS
3.3 | Accommodate the Higher Link Speed | Yes | More buffer space is required to server more service bursts accordingly. It's almost impossible to cause burst storm by a single interfering frame.
3.4(1) | Be Scalable to the Large Number of Flows | Partial | Shaping of CBS is based on serveral traffic class for aggregated flows. May need re-shaping (ATS) to avoid burstiness cascade for each class [1].
3.4(2) | Tolerate High Utilization | Yes | Set the pre-configuration of bandwidth limit for each traffic class. BE flows can use the unused portion of the reserved bandwidth of TSN flows.
3.5 | Prevent Flow Fluctuation from Disrupting Service | Yes | Each service flow of class A/B is permitted based on bandwidth reservation. The total amout of bandwidth reservation does not exceed the pre-configuration limit, and not exceed the worst latency.
3.6 | Tolerate Failures of Links or Nodes and Topology Changes | N/A | Not related to queuing mechanisms directly.
3.7 | Be Scalable to a Large Number of Hops with Complex Topology | Partial | On each node the queueing delay is over-estiamted, basically inversely proportional to the idle slope, due to non work-conserving behavior. Thus the E2E delay is large.
3.8 | Support Multi-Mechanisms in Single Domain and Multi-Domains | N/A | Not related to a single queuing mechanism directly.
[1] Latency and Backlog Bounds in Time-Sensitive Networking with Credit Based Shapers and Asynchronous Traffic Shaping (https://ieeexplore.ieee.org/document/8493026/)
CBS (Credit-Based Shaper), refer to IEEE 802.1Qav

## Slide 5
05
ATS Evaluation
section | Requirements | Evaluation | Notes
3.1 | Tolerate Time Asynchrony | Yes | Based on the ATS scheduler clocks,which is an implementation specific local system clock function. No need to achieve time synchronization.
3.2 | Support Large Single-hop Propagation Latency | Yes | Link delay does not affect asynchronous traffic shaping on per hop
3.3 | Accommodate the Higher Link Speed | Yes | More buffer space is required to server more service bursts accordingly.
3.4(1) | Be Scalable to the Large Number of Flows | Partial | ATS only maintain interleaved regulators (IR) per “inport + traffic class”. However, it need to maintain per flow states.
3.4(2) | Tolerate High Utilization | Yes | Can achieve high bandwidth utilization.
3.5 | Prevent Flow Fluctuation from Disrupting Service | Partial | The cost of interleaved regulators (IR) maintained per hop is high. The problem of IR head-of-line blocking should be considered.
3.6 | Tolerate Failures of Links or Nodes and Topology Changes |  | Not related to queuing mechanisms directly.
3.7 | Be Scalable to a Large Number of Hops with Complex Topology | Partial | Need to consider flow aggregation strategies at intermediate nodes. End-to-end delay upper bound provided by ATS is larger, basically inversely proportional to the reserved bandwidth.
3.8 | Support Multi-Mechanisms in Single Domain and Multi-Domains |  | Not related to a single queuing mechanism directly.
ATS (Asynchronous Traffic Shaping), refer to IEEE 802.1Qcr

## Slide 6
04
CQF Evaluation
sectionc | Requirements | Evaluation | Notes
3.1 | Tolerate Time Asynchrony | No | Rely on nanosecond clock synchronization across the entire network, where all network nodes align their cycle boundaries.
3.2 | Support Large Single-hop Propagation Latency | No | Link delay must be much smaller than cycle duration and considered negligible, so 2-buffer mode can work. Otherwise, 3-buffer (or more) mode is needed.
3.3 | Accommodate the Higher Link Speed | Partial | More buffer space is required for a specific length of cycle duration.
3.4(1) | Be Scalable to the Large Number of Flows | Partial | Transmission gates are associated with each aggregated queue, but the stream filtering and policing actions per stream should be maintained.
3.4(2) | Tolerate High Utilization | No | The cycle duration includes a time zone called dead time (DT) contributed by Output delay, Link delay, Frame preemption delay, Processing delay, which can not be used to send packets.
3.5 | Prevent Flow Fluctuation from Disrupting Service | Partial | Requires corresponding flows setup algorithms to allocate resources appropriately among multiple flows to avoid transmission conflicts.
3.6 | Tolerate Failures of Links or Nodes and Topology Changes |  | Not related to queuing mechanisms directly.
3.7 | Be Scalable to a Large Number of Hops with Complex Topology | Partial | It is more difficult to select the cycle time. Need making trade-offs between end-to-end delay and cycle duration.
3.8 | Support Multi-Mechanisms in Single Domain and Multi-Domains |  | Not related to a single queuing mechanism directly.
CQF (Cyclic Queuing and Forwarding), refer to IEEE 802.1Qch

## Slide 7: Comments and Questions
Sections 3.3 and 3.4 in the requirements draft both mention considerations about flow aggregation. From a correlation perspective, it is recommended to merge this portion of section 3.3 into section 3.4.
How to understand the "high utilization" mentioned in section 3.4?
  “high utilization” may include two aspects:
  Allocate a portion of the bandwidth from the total bandwidth for deterministic flows, and the unused portion can be used by BE flows;
  Allocate a portion of the bandwidth from the total bandwidth for deterministic flows, and can be utilized sufficiently by deterministic flows as much as possible;
  Is it one of the two or both?
06

## Slide 8: THANK YOU